## Slide 1: FFAG Designs for eRHIC and Cb Return Loops
Stephen Brooks
Accelerator R&D Division, C-AD

## Slide 2: eRHIC Overview
Loops
1.7-5.0
6.7-20.0
1.67 GeV
arXiv:1409.1633

## Slide 3: eRHIC Motivation
The eRHIC ERL is passed through 24 times
  12 accelerating and 12 decelerating passes
  1.67GeV of linac can make 20GeV top energy
  FFAGs allow 2 return loops to hold 12 energies
Once-through nature of ERL means electron beam can have high interaction parameter
FFAGs use fixed magnetic fields for operation with continuous wave beams (like cyclotrons)

## Slide 4: FFAG Arc Cells Parameters
Parameter | FFAG1 (low energy) | FFAG2 (high energy)
Energy range | 1.667 – 5.000 GeV | 6.667 – 20.000 GeV
Energy ratio | 3.00× | 3.00×
Turns (1.666…GeV linac) | 3 | 9 (or 8 + separate turn)
Synchrotron power (* L=2138m arcs) (* I=-10mA) | 0.009MW | 3.89MW @ 20GeV 1.63MW @ 15GeV 0.62MW @ 10GeV
TOF range | 30.1ppm (6.4cm) | 35.3ppm (7.5cm)
Long drift space | 40.0cm | 40.0cm
Tune range | 0.031 – 0.345 | 0.031 – 0.345
Orbit range (quads) | 19.6mm (rmax = 13.2mm) | 19.6mm (rmax = 13.2mm)
Max ¦B¦ on orbit | 0.114 T | 0.458 T
Max quad strength | 8.672 T/m | 34.686 T/m

## Slide 5: Orbits in Cells (Muon1 simulation)
Transverse exaggeration x64

## Slide 6: FFAG Arc Cells Lattice (2.78m long)
Element | Length (m) | Angle (mrad) | Gradient (T/m) | Offset (mm) *
BD2 | 1.004701 | 2.643951 | 34.686326 | -7.009056
DS2 | 0.2 | 0.526316 |  | 
QF2 | 1.179936 | 3.105095 | -34.686326 | 3.386913
DL2 | 0.4 | 1.052632 |  | * Relative to chord
Element | Length (m) | Angle (mrad) | Gradient (T/m) | Offset (mm) *
BD1 | 1.004701 | 2.643951 | 8.671581 | -7.009056
DS1 | 0.2 | 0.526316 |  | 
QF1 | 1.179936 | 3.105095 | -8.671581 | 3.386913
DL1 | 0.4 | 1.052632 |  | * Relative to chord
Provisional 3+9 turn lattice from Scott Berg
1.67GeV 648MHz linac/12 turns was a recent change. After this section, results are presented for the previous 1.322GeV 422MHz linac/16 turn design.

## Slide 7: Previous design high-energy FFAG

## Slide 8: Tunes

## Slide 9: Path Length and TOF

## Slide 10: Synchrotron Loss and Max B Field
If replaced by separate turn

## Slide 11: Historical High-Energy Cells
Parameter | Jan’14 (50T/m FODO) | Oct’14 (30T/m doublet) | Jun’15 (4+12 turns)
Energy range | 7.944 – 21.164 GeV | 7.944 – 21.164 GeV | 6.622 – 21.164 GeV
Energy ratio | 2.66× | 2.66× | 3.20×
Turns (1.322GeV linac) | 11 | 11 | 12
Synchrotron power (* L=2138m arcs) (* I=-10mA) | 5.44MW @ 21.1GeV 2.04MW @ 15.8GeV 0.64MW @ 10.5GeV | 4.95MW @ 21.1GeV 1.90MW @ 15.8GeV 0.60MW @ 10.5GeV | 6.31MW @ 21.1GeV 2.27MW @ 15.8GeV 0.92MW @ 10.5GeV
TOF range | 22.4ppm (5cm) | 38.0ppm (9cm) | 56.9ppm (12cm)
Drift space | 28.8cm | 45.0cm (and 6.0cm) | 18.0cm
Tune range | 0.035 – 0.369 | 0.033 – 0.410 | 0.024 – 0.346
Orbit range (quads) | 12.6mm (rmax = 9.1) | 21.6mm (rmax = 15.8) | 30.5mm (rmax = 21.7)
Max ¦B¦ on orbit | 0.451 T | 0.416 T | 0.467 T
Max quad strength | 49.515 T/m | 29.256 T/m | 28.870 T/m

## Slide 12: eRHIC FFAG Straight Sections
Orbits exaggerated transversely x1000
As dipole component disappears, all orbits move to straight centre line with small errors:
± 0.436 mm in low-energy ring
± 0.066 mm in high-energy ring
…that can be corrected with fine adjustments
High energy FFAG
Low energy FFAG
Quadrupole offsets and curvature adiabatically removed over 17 transition cells.
Scaling factor for each cell:
a = 3p2-2p3, p = cell#/18

## Slide 13: Arc-to-Straight Adiabatic Only
~0.1mm errors
Transverse exaggeration x2500

## Slide 14: Arc-to-Straight Improved
Fine-tuned using the 17 cells in the matcher
~2.5um errors

## Slide 15: Fine Tuning Dipole Fields (T)

## Slide 16: Muon1 Response Output
Muon1 simulation
Any constrained linear optimisation tool
Corrector vector
as lattice input
For each “ResponseBPM” j,
a CSV file containing the matrix:
Any attribute can become a corrector, e.g. adding a ResponseDipole=1e-6 attribute will vary that Dipole by 1e-6 Tesla in the numerical differentiation.
…and the uncorrected
positions:

## Slide 17: eRHIC FFAG Rings in Perspective
Orbits exaggerated transversely x5000, shape of hexagonal RHIC is evident

## Slide 20: Full Lattice Strategy: Outline
Break the FFAGs into sections
Each piece must be fine-tuned
MAD-X export has been developed
Muon1 can lay out whole ring overlaid on RHIC tunnel plan
  Also can output lists of survey coordinates

## Slide 21: FFAG Special Sections
Linac
Splitter/Combiner
Arc
Matcher
Straight
Crossover straight
Bypass straight

## Slide 22: Alternative Without Separate Pass
Linac
Splitter/Combiner
Arc
Matcher
Straight
Crossover straight
Extraction arc
Bypass straight

## Slide 23: Matched Section Names (r = ring #)
Linac
Splitter/Combiner
rA11
rM03
Straight
rC10
rA09
rB08
Zero datums
rC04
rA05
rB06
rM12
rA07

## Slide 24: Entry Energies (x = 60° SR)
Linac
Splitter/Combiner
Straight
E
E-x
E-x
E-2x
E-2x
E-3x
E-3x
E-4x
E-4x
E-5x
E-5x
The arc-like sections require smoothed SR loss option in Muon1
rA11
rC10
rB08
rC04
rB06
rA07
rA03
rA01
rA09
rA05

## Slide 25: Design Levels of Detail Level 1: Circle
Arc

## Slide 26: Level 2: Hexagon
Arc
Matcher
Straight

## Slide 27: Level 3: All FFAG Sections
Arc
Matcher
Bypass straight
Crossover straight
Straight

## Slide 28: Level 4: Closed ERL
Linac
Arc
Matcher
Bypass straight
Crossover straight
Splitter/Combiner
Straight

## Slide 29: Level 5: eRHIC Complete
Linac
Arc
Matcher
Bypass straight
Hadron ring (not shown)
Dump
Injector
Detectors
IR lines
Crossover straight
Splitter/Combiner
Straight

## Slide 30: Current Lattice Status
Jun’15 (4+12 turn, 422MHz) lattice has been taken to the level 2/“hexagon” level of detail
  This hexagon was tuned to fit in the RHIC tunnel
  This and the various Muon1 and MAD-X export files have been published to the eRHIC wiki
New cell for 647MHz (3+9 turn) only recently developed so is at the level 1/“circle” stage
  Publish to wiki coming soon

## Slide 31: Tunnel Crossover under RHIC Pipe
eRHIC path length must ~= RHIC hadron ring
  Can’t stay on inside or outside all the way around
Space under 4 and 10 o’clock no-cryo pipe
Adiabtic scheme similar to bypass gives 3.36m total horizontal displacement
30m central warm section with 1.81m displacement

## Slide 32: All Lines Going Through IRs
Hadron ring
Electron FFAGs
High-energy electron line
Greatly exaggerated!
Detectors moved inwards to allow bypass

## Slide 33: 3D Bypass Layout in RHIC Tunnel
Enough clearance for an R=4.16m (STAR-sized) detector if it is displaced inwards on existing rails by 1.76m. Clearances would be >34cm from beamline centre to walls/detector
Orbits exaggerated transversely x5000

## Slide 34: Detector Bypasses: a Flexible FFAG
Orbits exaggerated 2000x, beamline to scale
-Dq
Dq
Dq
Curvature
Bypass straight
Normal straight
Dq
-2Dq
Angle
Displacement
3.08m
76 cells
3
9
9
17
9
9
3
17
90.3m

## Slide 35: Detector CAD Model
electrons
ions
FFAG by-pass

## Slide 36: Detector CAD Model Zoom
Electrons
Ions
FFAG By-pass

## Slide 37: eRHIC IR v2.5, Layout Summary
Hadrons
Electrons
Synrad
The hadron beta functions are symmetric but the bending is antisymmetric.
Electron bending comes after the IP in order to avoid synrad background.
IP
Cryostat
Cryostat
Cryostat
Cryostat
Cryostat
Cryostat
Crab Cavities
Crab Cavities
Crab Cavities
Crab Cavities
Warm Quad
Warm Quad
4.5m Region
10 mrad total crossing angle
10 mrad additional electron bending
16 mrad hadron dogleg
16 mrad hadron dogleg has spectrometer function for forward going particles
ZDC
Yellow boxes outline the cold beam tube apertures.
Brett Parker’s design

## Slide 38: IR Forward Layout Details
Strong quadrupole focusing takes place in these, Q1 & Q2 apertures
Strong dipole bending in this B1 aperture
Low field “sweet spot” shielded
regions for incoming electrons in these apertures.
Note that the coordinate system in these figures is aligned with the center of the 4 mrad neutron cone (neutral vector) indicated by the hatched region on the plot.
4 mrad neutron cone acceptance

## Slide 39: IR Q1 Magnet Forward Details
Q1 Version 2.5 Parameters
Magnetic Length = 1.975 m
Main Gradient = 136.9 T/m
Field @ e-Beam < Few Gauss
The Version 2.5 Q1 magnet is longer than before and its aperture had to be increased to maintain desired forward experimental acceptance.
Note that the Q1 sweet spot region comes much closer to the main coil than the previous generic solution.
The Q1 outer coils contribute ~36% of the total gradient and the peak field now reaches 6.2 T on the main coil
Field quality is close to 1 x 10-4 at Rref=20mm (i.e. about 1 Unit).
Field inside elongated shielded region is less than 1 gauss in the main body.
Q1, Version 2.5 Optics, Full Model
Coil ends do not preserve the body cross section, so we must carefully optimize end turns. Combining magnetic and superconducting materials, “magnetic cloaking,” may be helpful. https://wiki.bnl.gov/eic/index.php/Magnetic_Cloak

## Slide 40: Electron IR lattice
3000
Triplet

## Slide 41: Hadron IR Lattice for b*= 5 cm
Doublet
Cold Regions
90⁰ phase advance and large b for Crab Cavities
While magnet apertures differ, the optics are the same for the forward and rear sides.
16 mrad “Dogleg Dipoles”

## Slide 42: FFAG Orbit Correction: Outline
Abstractly, FFAG “fine tuning” and actual orbit correction on the machine are the same
  Both use the linear response matrix
Practically, they differ
  BPM errors: position offsets, noise, nonlinearities
  Target differences to eliminate offset errors
    Between multiple beams going through the same BPM
    Distinguish turn-by-turn or during commissioning
  In arcs, can use double differences (this cell – last)

## Slide 43: Dispersion Correction is Important
Even energy spread ~ 10-3 in such a long channel can cause phase differences
  Of the order of 1000 cells around RHIC tunnel
  Natural chromaticity + errors  emittance growth
  Must correct orbits to within less than beam size
x’
x
x’
x
x’
x

## Slide 44: Projected RMS Emittance Growth
Convolution of beam shape with centroid scatter: s2projected = s2beam + s2centroids
Smallest sbeam ~= 25mm (in FFAG)
Keeping |scentroids| < 1mm would keep relative emittance growth below 1/252 = 1/625, which I think is tolerable, in every possible case
Larger errors depends on situation, 10mm might be OK, 100mm gives noticeable growth

## Slide 45: Field Error Sources
Field error source | Relative size | Equivalent displacement | Time scale | Linear / Nonlinear | Mitigation
Material magnetisation | 2e-2 | 200µm | Constant | Both | Magnet tuning on bench
Magnet assembly | 2e-3 | 20µm | Constant | Both | Magnet tuning on bench
Alignment on girder | 1e-2 | 100µm | Constant | Linear | 1% (50G) linear corrector coils
Radiation damage | <1e-3 | <10µm | Years | Unknown | 1% (50G) linear corrector coils
Temperature coefficient | 1e-3/K | 10µm/K | Minutes - hours | Linear (?) | Orbit feedback + corrector coils
Slow vibrations | <1e-3 | <10µm | < few Hz | Linear | Orbit feedback + corrector coils
Fast vibrations | <1e-5 | <0.1µm | > few Hz | Linear | Not corrected (small enough)
Model is appropriate
Appropriate if can respond as a function of time (“orbit feedback”)
Too large for 50G
Residual size OK
Independent beam errors are the worst case scenario, so model almost all of eRHIC’s errors

## Slide 46: Zero Energy Spread Situation
Log scale
“Perfect” at 42 cells, 84 correctors.
Just the beam centres with dp/p=0.
Still using 11 beams for this comparison;
6 to 8 beams should be easier.
Starting with beams randomly ~1mm off their orbits including errors in dispersion

## Slide 47: dp/p ±1e-3 Situation
Log scale
Residual offsets no more than 67nm using 94 cells, 188 correctors.
Emittance growth negligible from tracking.
4 orders of magnitude improvement
Each beam represented by 5 energies in dp range. All must be corrected to their closed orbit.

## Slide 48: dp/p ±1% Situation
Residual offsets no more than 0.35mm using 94 cells, 188 correctors.
Observe scaling of graph with dp/p.
Dominated by beam x errors
Dominated by first order dispersive errors
Higher-order region?

## Slide 49: Emittance Change for dp/p ±1%
5000 particles per energy in Muon1 tracking
No emittance change visible within statistics
  Average growth of beamlet -0.0188%

## Slide 50: Splitters
All 12 energies must be separated on either side of the linac to match the beta function from ~1m in the FFAG to ~100m in the linac
  If this was done adiabatically in an FFAG solution, the FFAG cells would have to be ~100m long!
Splitters also give:
  Path-length correction for every energy
  R56 control for longitudinal ERL match
  Position/launch tweaking for every energy

## Slide 51: Nick Tsoupas’ Splitter Layout
6.7 to 20 GeV Lines
1.7 to 5 GeV Lines
Updated for 1.67 GeV/12 turn ERL

## Slide 52
Splitting
section
Vert. Displ.
section
Hor. Achr.
Section
Begin Dx=0
Match-R56
section
R56/Path
section
Match-R56
section
Hor. Achr.
section
End Dx=0
Match to Arc
section

## Slide 53: Path Length Increase in Splitter
 | Energy [GeV] | Path_Increase [cm]
1 | 1.320 | 43.8
2 | 2.656 | 31.8
3 | 3.978 | 25.9
4 | 5.300 | 23.4
5 | 6.622 | 20.7
6 | 7.944 | 16.5
7 | 9.266 | 14.4
8 | 10.558 | 15.1
9 | 11.910 | 12.5
10 | 13.232 | 9.6
11 | 14.554 | 7.3
12 | 15.876 | 5.6
13 | 17.198 | 4.5
14 | 18.520 | 3.4
15 | 19.842 | 2.5
16 | 21.000 | 1.7
16 Lines 1.32 GeV ERL
 | Energy [GeV] | Path_Increase [cm]
1 | 1.67 | 31.5
2 | 3.34 | 26.0
3 | 5.00 | 16.1
4 | 6.68 | 14.9
5 | 8.35 | 12.8
6 | 10.02 | 9.6
7 | 11.69 | 7.4
8 | 13.36 | 5.4
9 | 15.03 | 4.4
10 | 16.70 | 3.3
11 | 18.37 | 2.40
12 | 20.00 | 1.55
12 Lines 1.67 GeV ERL
 | Energy [GeV] | Path_Increase [cm]
1 | 2 | 29.4
2 | 4 | 19.8
3 | 6 | 10.2
4 | 8 | 12.2
5 | 10 | 8.75
6 | 12 | 5.8
7 | 14 | 4.6
8 | 16 | 3.4
9 | 18 | 2.3
10 | 20 | 1.5
10 Lines 2.0 GeV ERL

## Slide 54: 16-turn Splitter in RHIC Tunnel
Perspective view of survey points

## Slide 55: 16-turn Splitter in RHIC Tunnel
End, beams merged into 2 stacked FFAGs

## Slide 56: eRHIC FFAG Lattice Future Work
Next ~2 months
  Agree on 12-turn lattice cell and publish to wiki
  Construct lattice to detail level 3/all FFAG sections
    Including export to MAD format and ELEGANT for tracking with collective effects
Next ~3 years
  Finalise IR line, splitters, linac, injector and dump
  Full end-to-end simulation (detail level 5)
  Add results to eRHIC CDR for CD-1 timeframe

## Slide 57: Cb Overview
Cb = CBETA = Cornell-BNL Energy recovery Test Accelerator
+/- 61 MeV
6 MeV
67, 128, 189, 250 MeV
6 MeV
Render by Chris Mayes (Cornell)
1.3GHz linac

## Slide 58: Cb Motivation
Cb will be the first accelerator in the world to include any of the following things, which are all required by the eRHIC design
  ERL using FFAG recirculating arcs
  Linear field FFAG with momentum range of 4x
  Adiabatic transition from curved to straight FFAG
  Permanent magnets (PMs) used in an FFAG
  NdFeB PMs used for main beam steering
  PMs used in ERL return arcs
  Multi-pass superconducting ERL
arXiv:1504.00588

## Slide 59: FFAG Arc Cells Parameters
Parameter | Cb FFAG (2015 version) | eRHIC FFAG2 (high energy)
Energy range | 67 – 250 MeV | 6.667 – 20.000 GeV
Energy ratio | 3.73× | 3.00×
Turns (1.666…GeV linac) | 4 | 9
Synchrotron power (* I=-10mA) | 0.000007MW | 3.89MW @ 20GeV 1.63MW @ 15GeV 0.62MW @ 10GeV
TOF range | 3.32 × 10−3 (10.9cm) | 35.3ppm (7.5cm)
Long drift space | 8.99cm | 40.0cm
Tune range | 0.026 – 0.322 | 0.031 – 0.345
Orbit range (quads) | 29.1mm (rmax = 28.6mm) | 19.6mm (rmax = 13.2mm)
Max ¦B¦ on orbit | 0.623 T | 0.458 T
Max quad strength | 37.195 T/m | 34.686 T/m

## Slide 60: Orbits in Cells (Muon1 simulation)
Transverse exaggeration x1
ACTUAL SIZE
Grid is in cm

## Slide 61: Racetrack Layout (Muon1)
Transverse exaggeration x64

## Slide 62: Arc Cell Lattice (32.99cm long)
Element | Length (m) | Angle (mrad) | Gradient (T/m) | Offset (mm)
QF | 0.08 | 11.083899 | -37.195 | 2.444758
DS | 0.05 | 0 |  | 
BD | 0.11 | -73.915752 | 24.039 | 18.346488
DL | 0.0899 | 0 |  | 
This is the lattice we’ve been using for most of this year
It will be updated soon to account for co-optimisation with the magnet bores

## Slide 63: Tracking Through Fieldmaps
Muon1
B-MAD

## Slide 65: Layout in Cornell L0E Hall

## Slide 66: Splitter Layout
By Chris Mayes (Cornell), tracking in B-MAD

## Slide 67: Arc-to-Straight Match
76 MeV
146 MeV
216 MeV
286 MeV
Cell
Arc-to-Straight (10 cells)
Focus
8 cm
42.5 T/m
-0.104 T
Defocus
11 cm
-27.5 T/m
-0.5044 T
(m)
(m)
(m)
-3.6 deg
By Chris Mayes (Cornell), tracking in B-MAD

## Slide 68: Orbit Corrections
500 um rms x offset errors
SVD correction given BPM readings for separate beams and correction coils on every other dipole
Full FFAG arc
Full FFAG arc
By Chris Mayes (Cornell), tracking in B-MAD

## Slide 69: Schedule (Georg Hoffstaetter)
10/01/2016 Design and prototyping complete
10/01/2017 Construction complete with Cornell’s ERL linac
03/01/2018 4-pass ERL operation with low current
10/01/2018 4-pass ERL operation with high current
01/01/2019 eRHIC linac installation
07/01/2019 4-pass ERL operation with eRHIC linac
10/01/2019 4-pass ERL operation with high current
This is based on the monthly resolution of activities listed in the next pages.
Oct-15 | Nov-15 | Dec-15 | Jan-16 | Feb-16 | Mar-16 | Apr-16 | May-16 | Jun-16 | Jul-16 | Aug-16 | Sep-16 | Oct-16 | Nov-16 | Dec-16 | Jan-17 | Feb-17 | Mar-17 | Apr-17 | May-17 | Jun-17 | Jul-17 | Aug-17 | Sep-17 | Oct-17 | Nov-17 | Dec-17 | Jan-18 | Feb-18 | Mar-18 | Apr-18 | May-18 | Jun-18 | Jul-18 | Aug-18 | Sep-18 | Oct-18 | Nov-18 | Dec-18 | Jan-19 | Feb-19 | Mar-19 | Apr-19 | May-19 | Jun-19 | Jul-19 | Aug-19 | Sep-19
Design and prototyping |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  | Construction with Cornell's ERL linac |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 4-pass ERL operation with low current |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Beam studies and 4-pass ERL with higher current |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | eRHIC linac installation |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | low-current 4-pass ERL operation with eRHIC linac |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | high-current operation |  | 
We are here
Optional synergy phase with eRHIC SRF development program

## Slide 70: Cell/Magnet Co-optimisation
Recently beam-to-pipe clearance was increased from 6mm to 12mm

## Slide 71: Cb Future Work
Next ~2 months
  Find a consistent combination of: FFAG cell beam trajectories, vacuum chamber thickness, magnet apertures and corrector coil design
  Track with fieldmaps
    Adjust as necessary for realistic fringe fields etc.
  Use this to begin writing the Cb CDR document
Next ~3 years
  The entire project (see previous timeline)

## Slide 72: Backup

## Slide 73: FFAG Lattice Scaling* Laws
Scaling type (by factor a) | Length | Angle | Dipole | Gradient | Quad offset (=dipole/grad) & orbit excursion
Momentum (~energy) | 1 | 1 | a | a | 1
Machine radius | a | 1 | a-1 | a-2 | a
FFAG beta length (fixed bend radius, fixed cell tune) | a | a | 1 | a-2 | a2
FFAG arc-to-straight (=row 3/row 2) | 1 | a | a | 1 | a
FFAG radius with fixed orbit excursion and field (row 2*row 1/sqrt(row 3)) | a1/2 | a-1/2 | 1 | 1 | 1
* not scaling FFAG laws
I’m going to use this one to decrease the curvature while keeping focussing the same

## Slide 74
Response matrix

## Slide 77: Can Include Dispersive Energies

## Slide 78: Dispersive Energies No Fine Tuning

## Slide 79: Adiabatic eRHIC Extraction
If an entire top-energy electron ring is built, extraction is simply from the splitters
This scheme extracts from the FFAG and only requires about 1/3 of the ring circumference
FFAG orbits are separated by lengthening the cells, maintaining constant tunnel curvature
Eventually they are far apart enough to extract using septums

## Slide 80: FFAG Lattice Scaling* Laws
Scaling type (by factor a) | Length | Angle | Dipole | Gradient | Quad offset (=dipole/grad) & orbit excursion
Momentum (~energy) | 1 | 1 | a | a | 1
Machine radius | a | 1 | a-1 | a-2 | a
FFAG beta length (fixed bend radius, fixed cell tune) | a | a | 1 | a-2 | a2
FFAG arc-to-straight (=row 3/row 2) | 1 | a | a | 1 | a
FFAG radius with fixed orbit excursion and field (row 2*row 1/sqrt(row 3)) | a1/2 | a-1/2 | 1 | 1 | 1
* not scaling FFAG laws
I’m going to use this one to increase the orbit separation in eRHIC FFAG2

## Slide 81: Adiabatic Cell Expansion
Length factor goes as a = exp(3p2-2p3)
  p = cell#/Ncells, 0  1 in expansion section
  Then reverse (Ncells=30 so 60 in total, 56.4° angle)
Cells increase in length by factor e ~= 2.718
  Orbits separate by factor e2 ~= 7.389
Transverse orbit exaggeration x256

## Slide 82: The Expanded Cell
Element | Length (m) | Gradient (T/m) | Expanded Length (m) | Expanded Gradient (T/m)
BD | 1.271956 | 29.256 | 3.446989 | 3.983632
Short drift | 0.06 |  | 0.162599 | 
QF | 1.809009 | -25 | 4.902398 | -3.404115
Long drift | 0.45 |  | 1.219496 | 
Separation of highest energy turns is 2.18cm
  Total orbit range ~14cm
  Enough room for septum for upper half of orbits
Original cell had 3mm separation, ~2cm range

## Slide 83: Extraction Arc Including Matchers
Straight-to-arc [17 cells], Expand orbits [30], Contract orbits [30], Arc-to-straight [17]
  So I can launch and collect particles at x=x’=0!
Only the central 30+30 corrected to begin
Transverse orbit exaggeration x512

## Slide 84: Emittance Growth Model Setup
The 11 beams are tracked through an extraction sextant to test for nonlinear-dispersion-related emittance growth
dp/p of ±1e-3, uniform distribution
20 mm.mrad initial normalised emittance
  Transverse Gaussian distribution
  Beams initially have matched bx,y, ax,y functions
5000 particles per beam

## Slide 85: Example Before/After Correction
Uncorrected output beam centroids
Moderate emittance growth of 0.13-15.75%
0.1-1mm errors
NB: from tracking rather than linear model of tracking; also contains statistical noise
x growth ranges from 0.002% to 0.030%
<5um errors

## Slide 86: Fine Tuning Strengths (T)

## Slide 87: Septum Design Example
Holger Witte’s permanent magnet septum design
0.7T vertical bending field
Field-free region for other beams
5mm septum thickness!
11mrad kick in 1.12m length for 21.2GeV beam

## Slide 88: eRHIC Septum Issues
Probably easier to kick beams horizontally in several cells to build up oscillation within pipe
Synchrotron radiation would hit the septum barrier so prefer “massless septum”
POP FFAG massless septum was only 0.1T
Design from Y. Iwashita, A. Noda of Kyoto U. achieves 0.8T although fit of field falloff within 2cm distance is marginal (some leakage)

## Slide 89: Iwashita/Noda Septum Design
Mitigations could include smaller aperture (±15mm is used here) and/or putting the penultimate beam on a field zero-crossing with zero integral rather than totally field-free

## Slide 90: Dynamics with Three “Septums”
Transverse orbit exaggeration x64
Purple = 21.2GeV (ignore others)
Septum positions:
10cm

## Slide 91: RHIC Pipe Crossovers in Tunnel
Space under 4 and 10 o’clock no-cryo pipe
Extracted electron beam 9-8 and 6-5 o’clock
E
E
E
Spin-preserving purely-vertical dog legs

## Slide 92: General Situation to be Corrected
Past errors have caused the beams to have pseudo-random errors in x and x’ centroids
  Phase advances very different for each beam
Dx and Dx’ errors also present from…
  Phase difference = Chromaticity of section * dp/p
  If intra-beam phase difference becomes large, higher-order D errors  likely emittance growth
Only consider X plane for now (no roll errors)
Use 50 Gauss horizontal dipole correctors
x’
x
x’
x
x’
x

## Slide 93: dp/p ±2e-3 Situation
Residual offsets no more than 68nm using 94 cells, 188 correctors.

## Slide 94: dp/p ±5e-3 Situation
Residual offsets no more than 0.13mm using 94 cells, 188 correctors.

## Slide 95
FFAG-bypass
Ion – Electron
Magnets
Cryostat
Crab Cavities
Detector
Solenoid

## Slide 96: IR Forward Layout Details
Note that the coordinate system in these figures is aligned with the center of the 4 mrad neutron cone (neutral vector) indicated by the hatched region on the plot.
Main Beam 3.5 mrad
4 mrad neutron cone
Q1
Q0
B1
Dp/p = 20% Po
3.5 mrad
ZDC
Forward
Detector
Roman
Pots
Dp/p = 50% Po
Measure as much as possible before the next cold accelerator region.
Q2, has HERA style “butterfly shape chamber”
Q2 Front

## Slide 97: eRHIC IR v2.5, Hadron Optics
Cold Region
Cold Region
Warm Region
90⁰ phase advance and large b for Crab Cavities
Smaller peak betas to reduce the chromaticity
While magnet apertures differ, the optics are the same for the forward and rear sides.
16 mrad “Dogleg Dipoles”
The Version 2.5 hadron beta function peaks are lower with respect to earlier optics in order to reduce the hadron beam chromaticity.
Neutrals and some forward off-momentum particles are detected within the first warm region shown here.
These optics are designed to be favorable for Crab Cavities.
We could look to design a secondary focus beyond 45 m.
Detection of forward particles after Crab Cavities seems ok.

## Slide 98: 16-turn Splitter in RHIC Tunnel
Start, near linac

## Slide 99: 16-turn Splitter in RHIC Tunnel
Beam separation

## Slide 100: 16-turn Splitter in RHIC Tunnel
Low and high energy in two different planes

## Slide 101: Tunes

## Slide 102: Path Length and TOF

## Slide 103: Synchrotron Loss and Max B Field

## Slide 104: Splitter Optics
By Chris Mayes (Cornell), tracking in B-MAD