## Slide 1: Fixed-Tune Non-Scaling FFAs
Design for RAL FETS-FFA (3-12MeV p)
Analysis for cell of two thin lenses

## Slide 2: Introduction
Recent studies by Dejan Trbojevic have confirmed that non-scaling FFAs can have their tune dependence on momentum flattened by adding non-linear components to the magnet fields, although not necessarily for an unlimited momentum range.
Quadrupole affects tune level, sextupole affects dQ/dp, octupole affects d2Q/dp2, etc.

## Slide 3: FETS-FFA requirements
3-12MeV protons
4m average radius
Several 1m drifts (one per cell here)
Fixed tunes: DQx,y<0.01 in ring, <0.001 per cell
Qx,y tunable over full range of 1 in ring
  For exploration of the tune plane in R&D
  I chose 12 cells so this is 1/12 range per cell
Geometrical aperture 1250mm.mrad (large)

## Slide 4: Algorithm
Runge-Kutta 4th order tracking step
Loop to get trajectory in cell
Finite difference to get transfer matrix
  Also gives tunes if orbit is closed
Iterate (Newton) to find closed orbit
Loop over all FFA energies
Finite difference parameters to get response matrix of tune functions to multipole changes
Iterate (optimiser) to find fixed-tune lattice
Muon1
Muon1 cell optics mode
Muon1 FFA optics mode
Fixed-tune FFA optimiser
(parallel)

## Slide 5: Field Model
Midplane field is product of:
  Transverse polynomial up to dodecapole
    Rough initial field coefficients up to octupole were found by Muon1 genetic algorithm before using fixed-tune FFA optimiser
  Longitudinal integral of Gaussian at both ends
    Fringe length given by s=6cm
Off-midplane fields extrapolated by repeated derivatives of this product of three functions

## Slide 6: Fixed-Tune Cell Orbits
Target cell tunes Qx=0.216, Qy=0.213

## Slide 7: Fixed-Tune Cell Fields
F field +0.15 to -0.43T, D field -0.42 to -0.02T

## Slide 8: Cell Tunes
Target cell tunes Qx=0.216, Qy=0.213

## Slide 9: Field Profiles
Only plotted in beam region, including sagitta
3MeV, ring inside 
 12MeV, ring outside

## Slide 10: Field vs. Kinetic Energy

## Slide 11: Field vs. Momentum
Average field should be proportional to momentum
Not exactly because I used “average” position in each magnet

## Slide 12: Gradient vs. Momentum
In a thin-lens model, the gradients should be proportional to momentum
Here they are not, I suspect edge focussing

## Slide 13: Tunes Beyond Energy Range
Target cell tunes Qx=0.216, Qy=0.213
Hits magnet bounding box

## Slide 14: Orbits Beyond Energy Range

## Slide 15: Beta x,y vs. Kinetic Energy

## Slide 16: Tune Range Requirement
Qx,y tunable over full range of 1 in ring
  For exploration of the tune plane in R&D
  I chose 12 cells so this is 1/12 range per cell
Qx=0.216, Qy=0.213 would be ring tune of (2.592,2.556)
So choose 2.5 to 3.5 ring tune range in both planes
  0.2083 to 0.2917 cell tune (all combinations)

## Slide 17: Four Tune “Corners”
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 18: Cell Tunes at Corners
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 19: Cell Tunes at Corners (zoom)
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 20: Field Profiles of Corner Designs
Qx=0.2083, Qy=0.2083
Qx=0.2917, Qy=0.2083
Qx=0.2083, Qy=0.2917
Qx=0.2917, Qy=0.2917

## Slide 21: Designs Summary Table
Cell Qx | Cell Qy | Max tune error | Max field (T) | Orbit range (m)
0.2083 | 0.2083 | 0.00074 | 0.5204 | 0.641
0.2083 | 0.2917 | 0.00185 | 0.6128 | 0.688
0.2917 | 0.2083 | 0.00168 | 0.4466 | 0.389
0.2917 | 0.2917 | 0.00037 | 0.4004 | 0.381
0.216 | 0.213 | 0.00126 | 0.4310 | 0.573
Qx low, Qy high corner is most “unnatural”
  Largest orbit excursion, highest field
    Had to let optimiser vary dipole to stay in magnet box
Higher Qx tunes greatly improve orbit range

## Slide 22: Half-way Interpolation Result
What happens if you average the fields (equivalently, multipole coefficients) between two of the corner designs?
  (0.2917,0.2083),(0.2917,0.2917)  (0.2917,0.25)?
Not so bad, especially at higher energies, but needs re-tuning iteration

## Slide 23: Horizontal Omni-Magnets
“Arbitrarily” configurable field By(x)
  Are their own correctors
Try flat 80cm-wide poles, 8cm full gap, with large embedded pole face windings
  20 windings each top and bottom
  2x4cm cross-section, 4cm horizontal pitch
Main 8x16cm H-magnet-style coil for dipole
Pole face windings return on nearest side
  Produce quadrupole if all have equal current
Round ones were described in my IPAC’13 paper

## Slide 24: Main Dipole Coil @ 5A/mm2
Roughly flat field, about 0.4T
2D designs in Poisson/SuperFish
(plots are in cm, Gauss)

## Slide 25: Single Pole Winding @ 5A/mm2
Produces ~0.1T field plateau to return side

## Slide 26: Qx=0.2083, Qy=0.2917 F magnet
0.613T peak field, “hardest case”

## Slide 27: Qx=0.2083, Qy=0.2917 F magnet
Winding current densities were found by SVD / least squares

## Slide 28: Qx=0.2917, Qy=0.2917 D magnet
0.404T peak field, only requires small part of aperture

## Slide 29: Qx=0.2917, Qy=0.2917 D magnet
SVD only activates coils in the region they have an effect

## Slide 30: Magnets Summary Table
Cell Qx | Cell Qy | Magnet name | Max current density (A/mm2) | Max By error (G) | Max field (T) | Orbit range (m)
0.2083 | 0.2083 | F | 2.090 | 2.25 | 0.5201 | 0.641
 |  | D | 3.111 | 1.98 | 0.3921 | 0.460
0.2083 | 0.2917 | F | 3.056 | 3.31 | 0.6126 | 0.688
 |  | D | 2.955 | 2.31 | 0.4260 | 0.471
0.2917 | 0.2083 | F | 3.073 | 2.23 | 0.4418 | 0.389
 |  | D | 3.189 | 1.89 | 0.3370 | 0.247
0.2917 | 0.2917 | F | 3.480 | 2.50 | 0.3883 | 0.381
 |  | D | 3.944 | 2.58 | 0.4035 | 0.224
0.216 | 0.213 | F | 2.372 | 1.88 | 0.4224 | 0.573
 |  | D | 4.256 | 2.32 | 0.4270 | 0.400

## Slide 31: Quick Dynamic Aperture Test
Started 8 particles at (x,y) = (±2.5/0,±2.5/0)cm
  Cell Qx=0.216, Qy=0.213 design
Tracked in ring for 60ms, all survived
Some particles at 3cm did not
Can use e = xinj2/binj to get apertures
Energy | Cells (in 60ms) | Turns | ex (geom.) | ey (geom.)
3MeV | 697 | 58 | 471 | 428 mm.mrad
6MeV | 954 | 79 | 408 | 374 mm.mrad
12MeV | 1266 | 105 | 381 | 365 mm.mrad

## Slide 32: Dynamic Aperture Notes
FETS-FFA request was 100mm.mrad normalised at 3MeV (bg=0.080)
  = 1250 mm.mrad geometric
by = 1.46m at 3MeV injection point
  Implies y = ±4.27cm (or ±5.31cm at maximum by)
  Larger than the magnet aperture (±4cm)!
This DA is not the painted beam size, it is a stability margin (all beam ≤ 250 mm.mrad)

## Slide 33: Analytic Method for 2 Thin Lenses
Assume small-angle (paraxial) approximation
  Weak focussing and edge focussing are negligible
  Not valid for the FETS-FFA example!
Fixed cell tunes with two lenses implies constant normalised focussing strength with momentum in each lens
  Qx, Qy are two constraints on linear optics and the focussing strengths (gradients) are two variables
For the case with 3 lenses and 2 constraints, see my IPAC’11 paper

## Slide 34: Function Variable Elimination
xF(p)
xD(p)
x’1(p)
x’2(p)
qF(p)
qD(p)
bF(x)
bD(x)
Four constraints from linear tracking at each energy (and closure)
Two constraints from constant normalised gradient assumption
...becomes the differential equation
Two constraints from rigidity relation
Normalised b = q(Bℓ)
Ends at qcell, Dxcell (constants)
d1
d2
F
D

## Slide 35: Change to Geometric Variables
Rigidity: pq(p) = b(x(p))
Constant norm. gradient: b’(x(p)) = kp
dRigidity/dp: q(p) + pq’(p) = b’(x(p))x’(p)
Therefore: q(p) + pq’(p) = kpx’(p) [= kDx(p)]
x dependency and b have been eliminated
The rest is easy
  Linear algebra
  Solving a 1-variable differential equation
See https://stephenbrooks.org/ap/report/2022-3/fixedtune2.pdf

## Slide 36: Two Thin Lenses Result
The general solution:
C=0 corresponds to straight scaling FFA
  Constant angle, logarithmic orbit position
Range of other solution families are possible
gives field profile implicitly
(arbitrary choice of x origin)

## Slide 37: Example
C values:
Approximately the FETS-FFA parameters but not the same machine (not paraxial)
Negative values of C here produce fields that cross zero like non-scaling FFAs

## Slide 38: Conclusion
Found fixed tune lattices to ~0.001 in cell tune
  And automated: eliminated most hand-tuning!
Dynamic aperture low by factor 2-3× in e
  Not small by most standards: >400mm.mrad
  Haven’t explored the full tune plane yet
Magnetic efficiency about twice as good as (spiral) scaling FFA, magnets buildable
  ~0.6T max field on beam vs. ~1.2T
Very interesting machine type

## Slide 39: Future Work
Dynamic aperture search of tune plane
  And maybe other parameters like fringe length or magnet edge angles (rect vs. sector etc.)
Try expressing transverse field as something better-conditioned than polynomials
  Like Fourier series, or Chebyshev polynomials
Maybe investigate low-level tune “noise” in Muon1 tracking/optics algorithm
  Could also be field model nonsmoothness