## Slide 1: VFFA Optics and Magnets
FFA Scaling Laws
VFFA Superconducting Magnet
VFFA Proton Accelerator
Isochronous 3D Cyclotrons
VFFA Electron Accelerator
VFFA Permanent Magnets
VFFA Electromagnets

## Slide 2: I. FFA Scaling Laws

## Slide 3: Features to Categorise FFAs
Transverse
  Magnetic field (linear, scaling or other nonlinear)
  Orbit motion (horizontal, vertical, diagonal)
  Tune variation (fixed, quasi-fixed or varying)
  Lattice cell (FODO, doublet, triplet, pumplet…)
    Does it use edge angle focussing? (then can use singlet)
Longitudinal
  Time of flight (fixed, quasi-fixed or varying)
  RF acceleration (pulsed or continuous wave)
Often called “isochronous”

## Slide 4: Why Does the Orbit Move?
Orbit position is determined by an equilibrium effect: finding a stable closed orbit
  It is not directly “centrifugal force” pushing the beam outward at higher energy
Q: can you design a machine where the orbit moves inward with increasing energy?
Q: can you design a machine with two stable closed orbits?
  These exercises are tricky, maybe try them later
(Slides can be downloaded online)

## Slide 5: Scaling Law
Suppose a magnetic field obeys the scaling law B(ax) = akB(x)
  For any a>0. This is a “continuous symmetry”
Q: how do the sizes of closed orbits in such a field change with momentum?
  Use the Lorentz force law F = q(E + v×B)
How do the tunes vary with momentum?
Are any other forms of scaling law possible?

## Slide 6: Other Scaling Laws
Scale
Translate vertically
+ rotate
B ∝ rk
B ∝ eky
B(r, q+t ln r) ∝ rk
B(y, q+ty) ∝ eky
General case: B(T ax) = eaB(x), T any translation + rotation + scaling

## Slide 7: Scaling FFA Problem
Just consider the radial direction so the scaling law becomes B(ar) = akB(r)
  Or by changing variables, B(r) = (r/r0)kB(r0)
Exercise: differentiate this with respect to r
B’ has the same sign as B
Defocussing magnets are reverse bending!
  “Circumference factor” C=|B|max/Bavg
To close a ring, must have more F than D

## Slide 8: Scaling FFA Lattice Search Example
April 29, 2019
Estimated dynamic aperture (log)
Magnetic efficiency
0.36T
0.33T
0.47T
0.57T
0.82T
0.29T
September 10, 2023
Stephen Brooks, FFA’23 Workshop
Field ∝ C

## Slide 9: II. VFFA Superconducting Magnet

## Slide 10: Horizontal Aperture SC Magnet
Getting vertical B field requires same-direction current windings on opposing sides
By proportional to x/(a2+x2): cancels at x=0!
a

## Slide 11: Constructive Interference
Getting horizontal B field requires opposite current windings and is easier
Bx proportional to a/(a2+x2)
a

## Slide 12: Vertical Aperture SC Magnet
But now the field is in the wrong direction!
That's OK, rotate the magnet
The dipole field is there
But what sort of focussing does this magnet give?

## Slide 13: “Scaling” VFFA Magnet
Dipole field should increase moving up the magnet, so set By = B0eky on axis (x=0)
Subtracting dipole component leaves the field of a skew quad:
Exponential is good because moving upwards just scales the field and all gradients
Thus closed orbits at different momenta are exactly the same shape, just translated upwards
VFFA = Vertical orbit excursion FFA

## Slide 14: Scaling VFFA Field & Scaling Law

## Slide 15: FODO Scaling VFFA Machine
First VFFA tracking simulation, for HB2010
  2D, zero space charge, nonlinear magnets
150mm.mrad egeom input beam
Proton-driver-like but nasty circumference factor! (C=17)

## Slide 17: Scaling VFFA with Mismatch

## Slide 18: VFFA Acceleration

## Slide 19: 2D Winding Model for Magnet

## Slide 20: Application: Hadron Therapy?
Low intensity but high rep-rate machines
  Fixed field useful, space charge not too bad
Small beams
  The VFFA magnet can be a narrow vertical slot
  Less stored energy, smaller windings required
Fixed tune allows slower acceleration, less RF
Disadvantage: we still have the FFA extraction-from-an-orbit-that-moves problem

## Slide 21: Historical References
“FFAG Electron Cyclotron” (Ohkawa, 1955)
  T. Ohkawa, Physical Review 100 p.1247, abstract (1955)
  Talk on isochronous electron VFFA with exponential field, with and without edge focussing
“Helicoidal FFAGs” (Leleux, 1959)
  G. Leleux, J. Proy and M. Salvat, Rapport OC 70, Service de Physique Appliquee Section d’Optique Corpusculaire (1959)
  Linear optics analysis of VFFA
“Accelerators with Vertically Increasing Field” (Teichmann, 1960-2)
  J. Teichmann, translated from Atomnaya Énergiya, Vol.12, No.6, pp.475–482 (1962)
  Isochronous, fixed tune electron VFFA, exponential field, suggestion of curved orbit excursion

## Slide 22: III. VFFA Proton Accelerator

## Slide 23: Motivation: ISIS Energy Booster
FFA to accelerate the 50Hz pulsed ISIS beam
Energy: 800MeV – 12GeV
Superconducting magnets
Ring radius 52m (2x ISIS) could do 2.5x,3x
Mean dipole field in magnets 0.47 – 4.14T
30% RF packing, 20% magnets, 2-4m drifts
Warm 6.2 – 7.3MHz RF
Harmonic number 8 (10,12 in larger ring)

## Slide 24: Scaling Law Problem
Defocussing requires reverse bending, as in scaling FFAs  large circumference
Searched for “lopsided” scaling VFFA lattices with good dynamic aperture [HB2010]
  10000 particles were tracked for 1km
  Survival rate plotted on axes of lengths of “F” and “D” type magnets
  This reveals both the lattice stability region and resonance stop-bands

## Slide 25
C = ∞ on diagonal

## Slide 26
C = ∞ on diagonal

## Slide 27: Lattices can't be very lopsided
Unfortunately in all cases the region of dynamic stability sticks very close to the F=D diagonal line
The 2nd FDF stability region does not have enough dynamic aperture
So basic scaling VFFAs will always be big, with much reverse bending
  Could edge focussing avoid reverse bends?

## Slide 28: Vertical Edge Focussing [HB2012]
Superconducting magnets allow this to be smaller than synchrotron designs at lower energies

## Slide 29: VFFA with Edge Focussing
y
z
z=0
z=L
q
t = tan q
z = z – ty
Scaling law:

## Slide 30: Spiral Scaling VFFA Magnet Field
5GeV
800MeV

## Slide 32: Cell Beta Functions
Doublet focussing nature
  Visible in u,v planes
FfD
  Doublet controlled by t
  Singlet controlled by k
Ring tune sensitivity:

## Slide 36: 12GeV VFFA RF Programme

## Slide 37: Longitudinal Intensity Effects

## Slide 39: References
“Vertical Orbit Excursion FFAGs”, S. Brooks, Proc. HB2010
“Acceleration in Vertical Orbit Excursion FFAGs with Edge Focussing”, S. Brooks, Proc. HB2012

## Slide 40: IV. Isochronous 3D Cyclotrons

## Slide 41: Isochronous Cyclotron Problem
Mean radius must satisfy r = bR
  Where R = c/2pfrev is the limiting radius as v  c
Mean By = p/qr = mbgc/qbR = g(mc/qR) = gB0
This produces a quadrupole as radii bunch up:
  dBy/dr = (B0/R)dg/db = (B0/R)bg3
Momentum only increases with bg
  Eventually quadrupole overfocusses the beam
  Energy limit for any given planar cyclotron
Normalised quadrupole ∝ g2

## Slide 42: Tilted Orbit Excursion
 Teichmann (1962) also had idea

## Slide 45: Future Work
Better alignment between the reference plane and the orbits, giving better convergence
Field adjustments to improve isochronism from the current ±0.62% variation
Vary qedge with energy to improve tune control
Make space for RF by using fewer sectors and/or more field-free space between sectors
Find an example superconducting winding scheme
Build electron model of the 3D cyclotron

## Slide 46: Conclusion (II,III,IV) & Applications
Non-isochronous proton VFFAs provide rapid cycling, high fields and compact SC magnet designs
  Neutron, neutrino and hadron therapy sources
Isochronous proton 3D cyclotrons promise cyclotron-like CW acceleration above 1GeV
  High cross sections for nuclear/spallation reactions
  Nuclear waste transmutation, isotope production
Electron VFFAs are already almost isochronous
  Multi-pass VFFA-ERL-FELs with only one recirculating arc

## Slide 47: V. VFFA Electron Accelerator

## Slide 48: Project Description
Design and risk-reduce a fixed-field accelerator (likely using permanent magnets) to produce the 18GeV electron bunches for eRHIC instead of an RCS. This eliminates most magnet power supplies and allows a faster acceleration cycle of ≤100 turns, giving a shorter RF pulse and easier spin preservation.
  Cost comparisons showed ~30% cost savings in overall accelerator using eRHIC and CBETA data

## Slide 49: Additional Applications
~mA level electron current could be available at BNL at 18GeV
  Comparable to SLAC
  Can allow beam physics experiments far beyond current ATF reach (70MeV)
Cyclotron-like behaviour at far higher energies
  Flexible time structure
VFFA principle applied to proton machines
  Currently being considered for 1.2GeV neutron source upgrade at RAL
  Forms the basis for waste transmutation “3D cyclotron” facility
    S.J. Brooks, Vertical orbit excursion fixed field alternating gradient accelerators, Phys. Rev. ST Accel. Beams 16, 084001 (2013)

## Slide 50: Arc Lattice Cell Candidates
Estimated dynamic aperture (log)
Magnetic efficiency
0.36T @ 18GeV
0.33T
0.47T
0.57T
0.82T
Field By=B0e-ky
Scaling law means focussing and bending have the same sign
Overall radius and top energy are fixed parameters, vary lattice and amount of reverse bend
Heuristic √bmaxe ≈ 0.1/k
e ≈ 0.01/(k2bmax)

## Slide 51: Full-Scale Lattice Cell

## Slide 52: VI. VFFA Permanent Magnet

## Slide 53: Demo Magnet Design
k = 20m-1
GFR = ±25mm
Bmax = 0.3T
L = 120mm
  5 slices of 24mm
  Using left-over 26x20x24mm blocks from CBETA magnet R&D
(Good Field Region)

## Slide 54: Geometry Optimisation

## Slide 55: 3D Printing from Design

## Slide 56: One-piece assembly doesn’t work: blocks roll around in channel

## Slide 57: Single 24mm-thick Layer

## Slide 58: Slice Repulsion: Need Longer Rods!

## Slide 59: Assembly of Repelling Slices

## Slide 60: BNL Rotating Coil Measurement
3D-printed shim holder

## Slide 61: Harmonics (untuned)
Measured
Ideal
Errors
Units: 10-4 of main harmonic at measurement radius R=25mm
(Header line)
Dipole
Quadrupole
Sextupole
Octupole
Decapole
Dodecapole
14-pole
16-pole
18-pole
20-pole
22-pole
24-pole
26-pole
28-pole
30-pole
32-pole
34-pole
36-pole
38-pole
40-pole

## Slide 62: Harmonics (tuned)
Measured
Ideal
Errors
Units: 10-4 of main harmonic at measurement radius R=25mm
(Header line)
Dipole
Quadrupole
Sextupole
Octupole
Decapole
Dodecapole
14-pole
16-pole
18-pole
20-pole
22-pole
24-pole
26-pole
28-pole
30-pole
32-pole
34-pole
36-pole
38-pole
40-pole

## Slide 63: Field and Error (untuned)
Field (T)
Field error (T)

## Slide 64: Field and Error (tuned)
Field (T)
Field error (T)

## Slide 65: Gradient and Local k (untuned)
Gradient (T/m)
k value

## Slide 66: Gradient and Local k (tuned)
Gradient (T/m)
k value

## Slide 67: Extension of Design Height
k = 20m-1
GFR y = -25mm to +175mm
Bmax = 0.3T
Max field error ~3 Gauss

## Slide 68: Demo Straight Section (1-72MeV)

## Slide 69: 4×4 Transfer Matrix
Usual (x,x’,y,y’) basis
(u,u’,v,v’) basis

## Slide 70: Demo Straight Cell Tunes, Height
y (m)
Cell tunes

## Slide 71: Demo Straight Cell Input Steering
x’ (rad)
x (m)
y’ (rad)
~= 0
Energy (MeV)

## Slide 72: Bent Demo Cell Attempt

## Slide 73: Bent Cell Tunes, Height
y (m)
Cell tunes

## Slide 74: Bent Cell Input Steering
x (m)
x’ (rad)
y’ (rad)
Energy (MeV)

## Slide 75: Bent Cell Input Optical Functions
bu,v (m)
au,v (m)
Energy (MeV)

## Slide 76: Another way: HalbachArea tool
We made a circular VFFA permanent magnet design in November 2023 when I last visited Kyushu U., using this tool:
https://stephenbrooks.org/ap/halbacharea/
This automatically designs permanent magnets with specified field harmonics.

## Slide 77: Conclusion (V, VI)
VFFAs with permanent magnets are very well suited for high-energy electron machines
  Fields are low to avoid synchrotron radiation, means permanent magnets are applicable
  Beams are small, so dynamic aperture in the VFFA is not a bad constraint, so magnets can be reasonably sized
  Designs even exist where all magnets are below beam synchrotron radiation plane

## Slide 78: Risks to be Investigated
Simulation:
  Dynamic aperture (non-linear magnetic fields)
  Spin preservation (100 turns is semi-fast acceleration regime)
  Lattice integration (arc-to-straight, linac section)
Experimental:
  Magnet field errors
  Alignment errors after correction (e.g. with piezo movers)
    Before correction is well-known, surveyors can do 100-200um easily
  Verify VFFA and high-phase-advance lattice works in practice (ATF beamline)

## Slide 79: References
Fixed-field accelerators
  Acceleration in the linear non-scaling fixed-field alternating-gradient accelerator EMMA, S. Machida et al., Nature Physics 8, 243–247 (2012).
  CBETA website: https://www.classe.cornell.edu/Research/CBETA/WebHome.html
  CBETA Design Report, Cornell-BNL ERL Test Accelerator, G.H. Hoffstaetter et al., https://arxiv.org/abs/1706.04245 [physics.acc-ph] (2017).
  CBETA note 032, The CBETA Fractional Arc Test, Ed. C. Gulliford, https://www.classe.cornell.edu/CBETA_PM/index_notes.html
VFFAs
  Vertical orbit excursion fixed field alternating gradient accelerators, S. Brooks, Phys. Rev. ST-AB 16, 084001 (2013).
  Vertical orbit-excursion Fixed Field Alternating Gradient Accelerators and 3D Cyclotrons, S. Brooks, Proc. IPAC’14 (invited talk)
Permanent Magnets
  Production of Low Cost, High Field Quality Halbach Magnets, S. Brooks et al., Proc. IPAC 2017.
  CBETA note 035, CBETA Halbach Magnet Production Run, S. Brooks
ATF fixed-field experiment
  ATF experiment AE-79 “Test of a Large Energy Acceptance NS-FFAG Arc at the ATF”,
  See also talk: Test of Linear-Field Non-Scaling FFAG Arc with a Wide Energy Range, S. Brooks, FFAG’17 workshop: https://indico.bnl.gov/event/2764/

## Slide 80: VII. VFFA Electromagnets

## Slide 81: “Omni-Magnet”
Many (12) independently-powered poles
Can produce any combination of multipoles if not too strong
“Configurable Field Magnets for a Proton Beam Dynamics R&D Ring”, S. Brooks, Proc. IPAC 2013

## Slide 82: VFFA Omni-Magnet
Exponential VFFA fields with k = 5m−1 (left) and k = 10m−1 (right)
Relative field accuracy better than 10−3 for B0 = 0.05T

## Slide 83: Multi-Coil Magnet at Kyushu U.
Chart: y [m]
After adjustment
Kyosuke Adachi, FFA’23