## Slide 1: Ultra-low Emittance Bunches from Laser Cooled Ion Traps for Intense Focal Points

## Slide 2: Ion Traps & Laser Doppler Cooling
Paul trap configuration has four AC transverse electrodes (like alternating gradient focussing) and DC longitudinal end caps
Temperature limit TD = ℏG/2kB = 0.552mK
Transverse trap electrodes
Longitudinal trap electrodes with injection / extraction hole
Ions
Laser
40Ca+
397nm photon
Emitted in random direction
Linewidth G = 2p*23MHz, frequency f = c/397e-9 = 755THz
Active over velocity range ~ c(23MHz/755THz) = 9.1m/s
Tune so that force pushes more on ions moving towards laser

## Slide 3: S-POD, IBEX experiments
Fluorescence of Coulomb crystal in S-POD trap, from K. Izawa et al., J. Phys. Soc. Jpn., Vol. 79, No. 12 (U.Hiroshima)
The IBEX Paul trap (RAL) with vacuum chamber opened. The four rods in the center of the image are the transverse trap electrodes.

## Slide 4: Laser Doppler Cooling Simulation

## Slide 5: Laser Doppler Cooling Simulation
N = 500 ions

## Slide 6: Ion Trap Flexibility
Flexible source with variable parameters over wide range:
  Bunch charge (1 to 107 ions)
    Via gas pressure, trap voltage
  Bunch size, aspect ratio, shape
    Via trap voltages, trap geometry, collimation
  Emittance/temperature
    Stop cooling part way, or tighten trap ( quantum limit!)
  Ion species
    Use sympathetic cooling - mix coolable ion e.g. 40Ca+ ion in contact with desired species
  Easily exchangeable electrode configurations
enorm,rms ≥ ℏ/2mc
Muroo et al., PTEP2023 063G01
IBEX 106-107
Martin et al., New J. Phys. 21 (2019) 053023
Takai et al., Japan. J. Appl. Phys. 45, No. 6A (2006) 5332-5343
S-POD 1-107

## Slide 7: Flexibility e.g.: 2D Coulomb Crystal
Made the transverse trapping voltages much smaller than the longitudinal

## Slide 8: What do we do with this beam?
x
p or gv
Typical ion source beam
x
p or gv
Parameter | Ion source | Ion trap
N | 109 | 500
enorm,rms | 10-7m | 2×10-13m
sx | 1mm | 90mm
sv | 30km/s | 0.65m/s
T | 4.3MK | 2mK
Parameter | Ion source | Ion trap
N | 109 | 500
enorm,rms | 10-7m | 2×10-13m
s*x | 9.4nm | 18fm
s*q | 10mrad | 10mrad
L/bunch | 9×1028cm-2 | 6×1027cm-2
Accelerate to
1000GeV/u
Focus with
sp/p = s*q = 0.01
Ion trap beam

## Slide 9: Analytic Model for High Specific Luminosity
Luminosity is held constant if N ∝ s*
  If s*q is also held constant, that’s N ∝ s* ∝ e
But luminosity per ion increases at smaller N
  6×1027cm-2 from 2×500 ions is 130,000 times more efficient than 9×1028cm-2 from 2×109 ions
In fact the ion trap saturated the cross section
  If stot > 84mbarn, then >500 collisions expected
  One pass and it’s gone!

## Slide 10: What’s going on in the longitudinal plane? and Other Questions
Need short bunch length for good collisions
  The ion trap’s emittance is small in all three planes
The bunch seems pretty “opaque”, does it self-interact?
  Space charge repulsion prior to the focus?
Why don’t collider interaction points create a sharp focus all three space planes?
  Is that even possible?
    Yes, but relativity reduces longitudinal Dvbunch rest frame

## Slide 11: Bunch Implosion Radius Limits
Model: imploding uniform sphere of charge in the bunch’s rest frame
Space charge dictates r ≥ 1/(4pe0) Nq2/Ek,in
  Ek,in is inward kinetic energy at sphere surface
  Density r ∝ N/r3 ∝ Ek,in3/N2
Emittance dictates sx ≥ enorm,rms/sbg
  sx = r/sqrt(5), sbg = (bg)in/sqrt(5)
sbg,Transv. = (bg)beams*q, sbg,Long. = bbeamsp/p

## Slide 12: Minor Complexities
Ca+ will behave as Ca20+ once nuclei are within each others’ electron clouds (no shielding)
Space charge forces for a non-spherical uniform charge density ellipsoid are actually coupled between the planes (but still linear)
  Just like the 2D KV envelope space charge force
  Integrated backwards from focal point and fitted focal ellipsoid size to match incoming s*q and sp/p

## Slide 13: Energy Scaling Graph
For N = 500 ions
sp/p = s*q = 0.01
Nuclear density 2.5e17
Water 1e3
Doesn’t quite get there, mainly because of longitudinal plane
Switch to using fully-stripped ion charge when orbitals touch

## Slide 14: Energy Scaling Graph
For N = 500 ions
sp/p = s*q = 0.02
eL = 1.9eT
Can fix by using a tighter ion trap with ~20× smaller emittance (not too hard) and 2× larger dp/p (helps a lot).
Colliding bunches could also work, as might an FFA channel supporting a wider dp/p.
Nuclear density 2.5e17
Water 1e3
“Nuclear spaghetti”

## Slide 15: Potential Future Applications
We can already accurately position objects close to the nuclear size (e.g. LIGO mirrors)
The low emittance (entropy) of the ion trap initial state allows nuclei to be placed in particular locations deliberately, e.g.:
  Make white dwarf, neutron star matter
  3-way and multi-way particle collisions
  Synthesise custom shapes of nuclear matter
  Possible neutron-rich superheavy elements
Deliberate placement of 35 Xe atoms in 1989

## Slide 16: Nonlinear Tracking Study: What can stop us?
Space charge, emittance and energy spread considerations as in analytic model
Optical aberrations!
  Lenses are not linear, spherical aberration, chromaticity etc.
Can focussing in all three planes be done?
Experimental noise, jitter etc.
  Ideas for feedback using scattered pattern from interaction point
    Coulomb scattering has very good resolution

## Slide 17: Focussing Beamline Simulation
Test of three-plane focusing and optical aberration correction (at lower energy)
  Input N=20000, T=2mK ion trap bunch parameters
  Given energy chirp
Curved electrostatic beamline
  Point-source ‘electrodes’
    Arranged in rings of 12
    Generalised multipole lenses
Goal: minimise 3D focal size

## Slide 18: Focussing Beamline Simulation

## Slide 19: Optimisation of Electrode Voltages
11 electrode charges were optimised per electrode ring (12 minus one monopole)
The bunch initial chirp was also optimised
So 15 electrode rings  166 parameters
Used modified Levenburg-Marquardt method with nonlinearity correction
  See https://arxiv.org/abs/2307.03820
    Response matrix  SVD  try various damped inverses
    Sample additional points to infer nonlinear behaviour

## Slide 20: Improved L-M Optimiser

## Slide 21: Focal Point Optimisation (T=2mK)

## Slide 22: Focal Point Optimisation (T=0)

## Slide 23: Focal Size vs. Electrodes Used
T=0 line shows limit from pure aberrations
Lines are limited by normalised emittance (const.) and chosen dp/p chirp (generally increasing)
Numerical accuracy floor?
“Theory” is the minimum allowed size taking account the emittance and chirp

## Slide 24: Focal Size vs. Energy
Beamlines with only one electrode ring stop here
Focal sizes plotted for all numbers of electrode rings
Two rings here
Higher energies don’t use 1% dp/p, could need more electrode rings or just be hitting numerical noise

## Slide 25: Optimal Chirp vs. Electrodes Used
As more beamline elements are allowed, optimiser can cancel aberrations for a larger momentum range
Higher energies have smaller geometrical emittance already, less incentive to increase dp/p

## Slide 26: Focal Size vs. Initial Chirp
Scalings as expected, ignoring 1TV that has a bit of trouble

## Slide 27: Other Options: Cooling at High Energy?
Doppler cooling also works in a boosted frame
Pros:
  Can create cold beams at or near final energy
    Bypass jitter from RF and acceleration process
  Use blue-shift to cool using harder transitions(?)
Cons:
  Needs a low-intra-beam-scattering (IBS) ring lattice
    Very low phase advance per cell
    Bunch velocity distribution near-Maxwellian
  Too much energy or field could strip ions
  Ring is more expensive than an at-rest ion trap
PALLAS ring did this, but beam velocity only 2.8km/s
Schramm et al., Plasma Phys. Control. Fusion 44 (2002) B375–B387
Improves cooling rate, but increases limiting temperature

## Slide 28: Increasing Current Throughput
Throughput of basic trap isn’t great
  107 ions every 16ms (62.5Hz) is 100pA average
But trap is small enough and 10ms is short enough that could make a CW cooling channel at a PALLAS-like speed of 50km/s
  Bunches every 100ns (10MHz), spaced by 5mm
    Average current could go as high as 16uA
  Length of channel 16ms*50km/s = 800m
    Could coil it up, trap can be narrow, rods few mm apart

## Slide 29: Recent Funding at BNL
Received Lab-Directed R&D (LDRD) funding at BNL, total $400k over 2 years, Oct ‘23-Sep ’25
  About $160k actual hardware after labour and overheads
Proposed to “construct a basic foundational system”
Probably without laser cooling to start with

## Slide 30: LDRD Hardware Current Status
In Bldg. 938 basement
Old RHIC polarimeter vacuum chamber has pumped down, leak free
Experimental platform for mounting inside chamber
Requisitions out for: MCP diagnostic, 500eV 100uA electron gun, turbopump system, oscilloscope, 150V/2kV/4kV voltage amplifiers.
Still need: arbitrary waveform generator, broadband voltage amplifiers, feedthroughs, Teflon parts.
3D printed + aluminium rods
1:1 model ion trap geometry

## Slide 31: Conclusion
Ultra-low emittance bunches provide some interesting unexplored regimes
  106 times smaller emittance vs. conventional bunches
  Extraction into an accelerator would be new
Lower entropy initial states are going to be the long term trend as experiments improve
Can even achieve the quantum ground state
  Produce e.g. entangled spin states in a beam!
Ultimately, appears capable of custom synthesis of nuclear density matter

## Slide 32: Beam sizes in focussing channel

## Slide 33: Doppler-cooled rings as of 2014
Noda et al., IPAC2014

## Slide 34: Visits to Labs in Japan November 2023
cERL, Fixed-Field Accelerators
and Ion Traps

## Slide 35: Locations
3
1
2
1 KEK
cERL 20MeV e- ERL
2 J-PARC
MR 30GeV p synchrotron
3 KURNS (formerly KURRI)
Kyoto University Institute for Integrated Radiation and Nuclear Science
150MeV p FFA
4 Hiroshima University
Ca+ ion trap,
~mK Coulomb crystals
5 Kyushu University (Ito Campus)
150MeV p FFA
40keV e- VFFA prototype
Tandem system
4
5

## Slide 36: Route of Nozomi Shinkansen
1
3
2
4
5

## Slide 37: 1. At KEK
Visited the cERL 20MeV 1-turn electron ERL
  Currently used for a variety of industrial applications
  Hiroshi Sakai is group leader
Plan was to participate in re-commissioning
  But cryo problem delay meant they were just starting as I had to leave!
  By end of November 2023, they had re-commissioned it to CW 0.9mA beam, near 100% energy recovery
  Results will be reported at ERL 2024 conference at KEK in September (they encourage us to attend)
Gave a seminar on CBETA operation, multi-turn orbit correction, path length correction, halo and degaussing

## Slide 38: cERL Control Room

## Slide 39: cERL electron gun
500kV DC photocathode gun
Vacuum pressure of 8e-12 mbar

## Slide 40: RF Section
Injector cryomodule (three 2-cell cavities) adds 2.5MeV for 3MeV total
Main linac cryomodule (two 9-cell cavities) adds/subtracts 17MeV for 20MeV total
All RF is 1.3GHz

## Slide 41: Arc Magnets
Trim dipole

## Slide 42: Arc and Experimental Side
Sextupole for chromaticity control
 Various experiments:
Wiggler for mid-infrared SASE FEL test
THz source (Resonant Coherent Diffraction Radiation)
Radioisotope production target

## Slide 43: 2. At J-PARC
Visit just for the morning, drive from KEK
  Chihiro Ohmori organised the tour
J-PARC control room
Tour of 30GeV “Main Ring” (MR)
Also magnetic alloy (MA) RF lab
J-PARC Main Ring is used for:
  Hadron Experimental Facility (K, p, m, n, L, pbar)
  Neutrino beam for T2K long baseline experiment

## Slide 44: J-PARC Control Room

## Slide 45: Machine Status
Cat is used to indicate operational mode

## Slide 46: Main Ring Dipoles

## Slide 47: Quadrupoles and Sextupole

## Slide 48: Vertical Dipole Steerer

## Slide 49: Skew Quadrupole

## Slide 50: RF Section
High-level amplifier
Magnetic alloy (MA) RF cavities

## Slide 51: Extraction Kickers

## Slide 52: Three-Way Split
To T2K target via superconducting bends
Main ring continues
Main ring dump

## Slide 53: Earthquake Effect
Displacement of a rubber seam between two concrete tunnel sections

## Slide 54: Magnetic Alloy RF Cavity

## Slide 55: Magnetic Alloy Material
Fine grooves are visible from the many layers

## Slide 56: 3. At KURNS
Kyoto University Institute for Integrated Radiation and Nuclear Science
  Formerly KURRI (Kyoto University Research Reactor Institute)
Yoshiharu Mori is group leader here
11 to 150MeV proton FFA
  Scaling type, triplet magnets
  Has been used for accelerator-driven reactor studies
  Copy of the one originally built at KEK
    Which is now moved to Kyushu University
  KEK had the first proton FFA system ever built
Gave seminars here on:
  Non-scaling fixed-tune FFA design
  Ultra-low emittance beams from ion traps
Discussion on mTRISTAN m-e Higgs factory. Very interesting and relevant to P5, look it up.

## Slide 57: 150MeV Fixed-Field Accelerator
 From 11MeV linac
1.5 to 11MeV booster FFA (middle) is no longer used
Ion-beta FFA with induction acceleration (old injector, no longer used)

## Slide 58: Extraction Line to Reactor

## Slide 59: Magnets
Each yoke actually contains three magnets: a DFD triplet.
This design saves power but field quality not great.
Wide vacuum chamber for orbit excursion


## Slide 60: Pole Shape for B ~ rk Scaling Field

## Slide 61: Ion-beta FFA
Central current windings for induction acceleration
This is actually a spiral scaling FFA!
Current leads for magnet pole face windings

## Slide 62: 4. Hiroshima University
Beam Physics Laboratory at Graduate School of Advanced Science and Engineering
  Lead by Hiromi Okamoto
Five Paul trap type Ca+ ion trap systems (S-POD I through V) have been constructed here
  One has laser Doppler cooling
    Can produce Coulomb crystals!
  Others are used to study beam physics
    Analogue simulation of space charge, resonances etc.
Discussions on hardware for my ion trap LDRD
Gave a seminar on ultra-low emittance beams

## Slide 63: Ion Trap Vacuum Chamber

## Slide 64: Four-Rod, Two-Section Paul Trap
Several geometries were tried at this lab

## Slide 65: Ion Cloud before Cooling
Camera acquires fluorescence signal

## Slide 66: Laser Cooling  Coulomb Crystal
Kento Muroo was operating the experiment
50-100 Ca+ ions seen here

## Slide 67: Longer Coulomb Crystal
Reducing the longitudinal trapping voltage makes the crystal longer

## Slide 68: Near-Spherical Coulomb Crystal
Increasing the longitudinal trapping voltage makes the crystal shorter and wider

## Slide 69: Wavemeter
Precise control of the laser frequency is needed to hit the Ca+ absorption line

## Slide 70: Laser

## Slide 71: 1D Coulomb Crystal (N=10)
This gives the smallest transverse emittance

## Slide 72: 1D Coulomb Crystal (N=9)
After a minute or more, an ion was lost.
“There was a collision”

## Slide 73: 5. Kyushu University
Center for Accelerator and Applied Beam Science, Ito Campus
  Group lead by Yujiro Yonemura
11 to 150MeV proton FFA, identical to KURNS!
  Some work on magnet field shimming
  Plan to bring protons and ions to an experimental hall in future
Vertical FFA prototype (under construction)
Parts of internal target (FFA-ERIT) ring for neutron source e.g. BNCT
Tandem and foil ion injection scheme
Here, I gave seminars on:
  Modified Halbach Magnets for Emerging Accelerator Applications
  High-Field Combined Function Permanent Magnet (>1.5T)
  Permanent Magnet VFFA for 18GeV Electron Acceleration
I also updated my HalbachArea magnet design software to output .comi input files compatible with Kyushu’s version of OPERA-3D

## Slide 74
Inner cyclotron provides 10MeV protons.
Tandem ion injector is interesting because it can do double stripping, for example:
He−  tandem foil  He+  injection foil  He2+
8MV

## Slide 75: Purple Version of KURNS FFA

## Slide 76: Large Slot Aperture MA RF Cavity
Water cooled
MA material

## Slide 77: VFFA Prototype Beamline
20-40keV electron gun
Four VFFA cells
Vertical steering, diagnostic #1
Diagnostic #2 

## Slide 78: VFFA Electromagnet Design
Scaling type FFA where the D magnet is also a reverse bend, so alternating bends
Iron frames with multiple independent coils to control field function

## Slide 79: Parts of FFA-ERIT
Eight sectors, stored in what will become the hadron experimental hall

## Slide 80: The ERIT Target (Beryllium Foil)

## Slide 81: Shim Plates for Magnets
Aim to locally control integral of field function B(r), whose derivative B’(r) controls the machine tunes

## Slide 82: Shim Plates Installed in One Cell

## Slide 83: Import of 2D Permanent Magnet from HalbachArea to OPERA-3D
This is actually a VFFA magnet
.comi file imported successfully

## Slide 84: Thanks for listening!