## Slide 1: Test of a Permanent Magnet NS-FFA Section with Fixed Tunes

## Slide 2: Introduction
Non-scaling FFAs can have their tune dependence on momentum flattened by adding non-linear components to the magnet fields, although not necessarily for an unlimited momentum range.
Quadrupole affects tune level, sextupole affects dQ/dp, octupole affects d2Q/dp2, etc.

## Slide 3: Application
Dejan Trbojevic proposes to accelerate protons in 10-250MeV range with a rapid cycle (100Hz-1kHz) for FLASH hadron therapy
  Many machine cycles within 100ms allow different energy (depth) slices to be done as well as being quick enough to trigger the biological FLASH effect
Need an FFA ring which also has fixed tunes
  But needs to fit in the hospital, so smaller than a scaling FFA  nonlinear fixed-tune NS-FFA

## Slide 4: ‘FLASH’ Proton Therapy facility: Stony Brook University Hospital – Radiation Oncology
6. D. Trbojevic, Title: “Non-scaling fixed field alternating gradient permanent magnet cancer therapy accelerator”, patent number: US 9661737 B2, Date of the patent: May 23, 2017 (belongs to the DOE). https://patentimages.storage.googleapis.com/42/5e/92/f7da1cf617d6e3/US9661737.pdf

## Slide 5: Fast Cycling Synchrotron Cycles
t(ms)
Kinetic
Energy
250
(MeV)
16.5-30
One synchrotron cycle
Ex.1
Ex.3
Ex.2
Injection
Energy
Second synchrotron cycle
0.8ms < t < 1.85ms
1.3kHz< f < 540 Hz
RF manipulation
Extraction #2
Time of bunch flight 405-550 ns
At the injection porch time of 926 ms there are 1680 turns. 15 turns for 15 Cyclotron bunches and 1650 turns for RF manipulations
Injection
Porch
If the RF kicks are 30 kV, during the slip-stacking merge a difference in the time of flight for two 2 energies is 773ps. If the batches are 15 m apart it would take 370 turns to get them aligned. Next step would be to merge into one bucket by snaping the new RF voltage on.
Extraction kicker wave forms

## Slide 6: Fast Cycling Acceleration with Ferrite cavities
 | Choices for injector cyclotron |  |  |  | Units
 | ACSI | GE | TR-19 | IBA | 
Energy of Injector Cyclotron | 14 | 16.5 | 19 | 30 | MeV
Cyclotron current | 400 | 200 | 400 | 1200 | mA
Treatment charge | 60 | 60 | 60 | 60 | nC
Injection turns | 4 | 4 | 4 | 2 | #
RF acceleration per turn | 29.70 | 29.70 | 29.70 | 44.55 | kV
Calculation | Treatments Options |  |  |  | 
Turn duration | 585.74 | 540.6 | 504.8 | 405.1 | ns
Charge per turn | 0.234 | 0.108 | 0.151 | 0.486 | nC
Charge per injection | 0.937 | 0.432 | 0.606 | 0.972 | nC
Machine cycles | 65 | 139 | 100 | 62 | #
Machine cycle rate | 540 | 540 | 540 | 809.95 | Hz
Outputs |  |  |  |  | 
Treatment time | 120 | 257 | 185 | 76.54 | ms
By Stephen Brooks

## Slide 7
Matching of the Multiple Energy Orbits to the Straight Section
3.5m arc radius in current design

## Slide 8: FFA Arc Cell Tunes
After iterative correction in Muon1, starting from an initial BMAD model, tunes are stable from 10MeV – 250MeV and nearly constant.
(Wiggly near low energy end because rigidity changes fast there).
Cell tune ranges:
Qx = 0.1608 ± 0.0004
Qy = 0.0738 ± 0.0011

## Slide 9: Magnet Field Profiles
Maximum fields equalised at 1.86T rather than 1.99T
“original” = BMAD model

## Slide 10: Peak Fields vs. Energy
Orange line is field at magnet longitudinal centre, which is different than at exit (orbit in fringe area) for D magnet.
D

## Slide 11: Orbits and Fields in Muon1

## Slide 12: Permanent Magnet Designs (F)
cm grid
NdFeB material
N42EH grade
Br=1.3T
69.90cm2 area
64.7 x 12mm aperture
Good field X±26.3mm
1.85T max field

## Slide 13: Permanent Magnet Designs (D)
NdFeB material
N42EH grade
Br=1.3T
93.88cm2 area
48.1 x 12mm aperture
Good field X±18.0mm
1.86T max field
cm grid

## Slide 14: Magnets Ordered from SABR Enterprises, LLC.

## Slide 15: Orbits within Magnets

## Slide 16: Test Beamline, 4 cells
Half-F magnets on each end
Angle 5.625° per cell,
4 cells = 22.5°
(1/8 of an 180° arc)
Cell length 34.4cm,
4 cells = 1.374m

## Slide 17: Test Beamline and Mounting

## Slide 18: Magnet Construction by Vendor
SABR Enterprises, LLC. in Massachusetts

## Slide 19: Beamline Assembly

## Slide 20: Magnet Apertures

## Slide 21: Fieldmap of one magnet

## Slide 22: Measured Integrated Field

## Slide 23: Corrected Integrated Field
Corrected via fit for Hall probe displacements and tilt angles

## Slide 24: Measured Gradients

## Slide 25: Attempt at Shimming
Shimming is possible in theory but more engineering is needed to keep wires securely in place in aperture, so magnets were not shimmed for this experiment.

## Slide 26: Camera and Beam Screen Plates
These were attached to both ends of the beamline.
4 cameras and 4 screens in total.

## Slide 27: Experiment at BNL beamlines
NSRL
  Protons 50-250MeV
  1 day 2 hours
Tandem
  Deuterons 12.9-28MeV
  Equivalent to protons 10-50MeV
    Via rigidity but also window/air energy loss calculation
    Tandem proton max energy is 28.75MeV
  1 day

## Slide 28: Installation (Tandem)
Different beam energies marked on a ruler for alignment.

## Slide 29: Calibration and 1s Ellipse Fit

## Slide 30: Dimmest Beam Fit
Also background frames were subtracted

## Slide 31: NSRL 250MeV protons
Beam in
Beam out

## Slide 32: NSRL 200MeV protons
Beam in
Beam out

## Slide 33: NSRL 150MeV protons
Beam in
Beam out
Obscured by stray light on screen 3

## Slide 34: NSRL 100MeV protons
Beam in
Beam out

## Slide 35: NSRL 70MeV protons
Beam in
Beam out

## Slide 36: NSRL 50MeV protons
Beam in
Beam out

## Slide 37: NSRL All Energies
Beam in
Beam out

## Slide 38: Tandem 28MeV d ~ 50MeV p
Beam in
Beam out

## Slide 39: Tandem 24.2MeV d ~ 40MeV p
Beam in
Beam out

## Slide 40: Tandem 20MeV d ~ 30MeV p
Beam in
Beam out

## Slide 41: Tandem 16MeV d ~ 20MeV p
Beam in
Beam out

## Slide 42: Tandem 14.3MeV d ~ 15MeV p
Beam in
Beam out

## Slide 43: Tandem 12.9MeV d ~ 10MeV p
Beam in
Beam out
Beam may have stopped in air before screen 4

## Slide 44: Tandem All Energies
Beam in
Beam out

## Slide 45: All 12 Ellipses
Beam in
Beam out

## Slide 46: Centroid X Positions
Beam in
Beam out

## Slide 47: Screens Attached in Random Places
This affected the Tandem run, so the screens were resurveyed and the offsets subtracted
Screen 1
Screen 2
Screen 3
Screen 4

## Slide 48: Corrected Centroid X Positions
Beam in
Beam out

## Slide 49: Centroid Y Positions
Known Y shift from reassembly of camera screens between NSRL and Tandem
Beam in
Beam out

## Slide 50: Attempt at Transfer Matrix Element
Not much time, but some energies were tried offset horizontally from the nominal entrance position by a few mm
  Often the entrance position of the previous energy was used with the next energy
dxout/dxin ~= (change in average X centroid position on output screens)/(change in average X centroid on input screens)

## Slide 51: Transfer Matrix Mxx Element
4Qx,cell = 0.644  cos(fx) = -0.618
Agrees at high energy, changes at low energy
  Could be injecting off the closed orbit  sextupole feed down
(Kind of surprised we got any valid data for this at all)

## Slide 52: Tracking Offset Trajectories
±10mm

## Slide 53: Matrix Element from Tracking
Looks sensitive to injection position especially at low energy
±10mm

## Slide 54: Filling the Dynamic Aperture?
At lower energies, the output beam gets very large and starts to assume a crescent shape

## Slide 55: Transfer Matrix Mxx Element Again
With the corrected centroids, use the difference of the beam position to the central orbit (according to survey) to derive a matrix element between input and output
  No longer calculated around an offset orbit!
  Looks more reliably negative, but noisier
  1mm centroid errors make large error bars on this

## Slide 56: Experiment Conclusion
Beams at all energies were transmitted through the 4-cell test girder (22.5° or 1/8 arc)
  Protons at NSRL and deuterons at Tandem
10-250MeV is a factor of 5.3× in momentum
  Very large for a non-scaling FFA, especially one with a flattened tune
  250MeV is highest ever energy in any NS-FFA line
Beam ought to propagate several cells around a ring at the start of commissioning
  (even without magnet shimming/correction here)

## Slide 57: Magnetic Efficiency
Circumference or field factor of 2.29× relative to ideal synchrotron

## Slide 58: Two Stage Machine
1.63× relative to ideal synchrotron
Momentum ratio 5.31=3.54*1.40, split at 135MeV k.e.

## Slide 59: Two Stage Machine Conclusion
The two stage machine reduces fields by a factor of 1.4, or same field at lower radius
  One stage FFA: 3.5m radius (7m diameter)
  Two stage FFA: 2.5m radius (5m diameter)
  Ideal synchrotron: 1.53m radius (3.06m diameter)
    But difficult to ramp the magnets at 100s of Hz
Quick design: just cut out pieces of the original machine’s momentum range and scale them!

## Slide 60: BACKUP

## Slide 61: Lattice Converted from BMAD
Multipoles dipole…dodeca
Three cells for field wrap
Angle 5.625° per cell, 64 cells per turn. Cell length 34.4cm, R=3.5m.
This worked well in BMAD, fixed stable tunes from 10MeV – 250MeV
These slides look a lot like last year’s, but Dejan’s multipole numbers have changed!

## Slide 62: BMAD and Muon1 Magnet Models
BMAD has a zero-length end field model
Muon1 has a Maxwellian fringe field model with finite length (bit more realistic)
  But you have to choose the length yourself!
  Only way to do this sort of field in BMAD is to generate fieldmaps, so there’s a difference
We also changed from sectors to rectangles but that turned out to be a small effect

## Slide 63: Field Profiles (BMAD)

## Slide 64: BMAD Lattice in Muon1
Vertical tune is unstable at low energies
  On previous lattice version, this was true no matter what Muon1 fringe field length I chose
MeV
Cell tune

## Slide 65: Peak Fields on Orbit (vs. Energy)
MeV
T
Interesting issue with D magnet: field on orbit never reaches its “infinite-length magnet” asymptotic value, so plot both
D

## Slide 66: This cell can be “easily” fixed using the Algorithm I used before
Runge-Kutta 4th order tracking step
Loop to get trajectory in cell
Finite difference to get transfer matrix
  Also gives tunes if orbit is closed
Iterate (Newton) to find closed orbit
Loop over all FFA energies
Finite difference parameters to get response matrix of tune functions to multipole changes
Iterate (optimiser) to find fixed-tune lattice
Muon1
Muon1 cell optics mode
Muon1 FFA optics mode
Fixed-tune FFA optimiser
(parallel)
Fourier coefficient

## Slide 67: Wait, Fourier coefficients?
Representing the transverse midplane field dependence By(x,0) as a Fourier series made optimisation work better than multipoles
  Suspect this is because sin,cos(nx) are orthogonal whereas polynomials are highly correlated
Used the form
By(x,0) = c0 + Sn=1..8 snsin(nkx) + cncos(nkx)
…where 2p/k is about twice the orbit excursion

## Slide 69: Magnet Sim. Field Error Graph (F)
3.6×10-4 relative error

## Slide 70: Magnet Sim. Field Error Graph (D)
1.6×10-4 relative error

## Slide 71: Magnet Holders Machined

## Slide 72: Magnet Holders Machined

## Slide 73: End Plates Machined