## Slide 1: The CEBAF 22GeV Energy Upgrade

## Slide 2: The Site

## Slide 3: The Site
Injector
North linac
South linac
Hall D
Halls A,B,C

## Slide 4: 6GeV “Original” CEBAF (2000)
(Actually started from 4GeV in 1995)

## Slide 5: 6  12GeV Upgrade (2017)
1.1GeV linacs
123MeV injector

## Slide 6
Still 1.1GeV linacs
6  11 passes each

## Slide 7: Energies of Each Turn
West arcs | East arcs
Injector = 123MeV | 1.2GeV
2.3GeV | 3.4GeV
4.5GeV | 5.6GeV
6.7GeV | 7.8GeV
8.8GeV | 9.9GeV
11.0GeV = Halls A, B, C | 12.0GeV = Hall D
West arcs | East arcs | SR loss per arc
Injector = 650MeV | 1.7GeV | 0.0070MeV
2.8GeV | 3.9GeV | 0.23MeV
5.0GeV | 6.1GeV | 1.6MeV
7.2GeV | 8.3GeV | 5.7MeV
9.4GeV | 10.5GeV | 20MeV
11.6GeV | 12.6GeV | 34MeV
13.7GeV | 14.8GeV | 39MeV
15.8GeV | 16.9GeV | 47MeV
17.9GeV | 19.0GeV | 70MeV
20.0GeV | 20.9GeV | 129MeV
21.9GeV = Halls A, B, C | 22.9GeV = Hall D | 186MeV
Above: 12GeV CEBAF
5+5 arc passes
5+6 linac passes to Hall D
Right: 22GeV upgrade
(4+6)+(4+6) arc passes
10+11 linac passes

## Slide 8: 650MeV Injector Upgrade
by Alex Bogacz and Salim Ogur

## Slide 9: 650MeV Injector Upgrade

## Slide 10: What is LERF?

## Slide 11: 12GeV CEBAF in the Tunnel

## Slide 12: Stacked Quadrupoles

## Slide 13: Stacked Dipoles

## Slide 14: Stacked Drift Spaces

## Slide 15: CW Superconducting Linac
1497MHz
2K
Nb

## Slide 16: Inter-tank Focussing Quadrupole

## Slide 17: Vertical Splitting Sections

## Slide 18: Vertical Splitting Sections

## Slide 19: Lines to the Halls

## Slide 20: Lines to the Halls

## Slide 21
Still 1.1GeV linacs
6  11 passes each

## Slide 22: Multi-Pass Linac Optics
Alternating FDF/DFD triplets
by Alex Bogacz

## Slide 23: Lowest Energy Linac Passes

## Slide 24: Higher Energy Linac Passes
Alternating triplets become FODO!

## Slide 25
Still 1.1GeV linacs
6  11 passes each

## Slide 26: The New FFA Arcs
A fixed field accelerator (FFA) is a low-dispersion line that can transmit a wide range of energies simultaneously (CEBAF is CW)
The lattice will hold six energies:
  East arc 10.5-21GeV
  West arc 11.5-22GeV
…while bending around the same average radius of curvature as the existing arcs

## Slide 27: FFA Arc Lattice Cell
BD
BF
1.245m length
-0.383T dipole +
43.44T/m gradient
1.673m length
-1.282T dipole +
-41.13T/m gradient
0.116m length drifts
3.150m total length
2.24° total angle
(80.4 per 180° arc)
80.6m bend radius
= CEBAF tunnel
Orbits to scale
Transversely exaggerated 16×
10.5GeV
21GeV

## Slide 28: Arc Cell Optics and Tunes

## Slide 29: Six Energies in FFA Arc Lattice

## Slide 30: Phase Spaces

## Slide 31: High-Field Combined Function Permanent Magnet
We prototyped an open midplane design with the following requirements:
  -0.9512T central field + 55.54T/m gradient
  ±10.5mm good field region
    Bmax,gfr = -1.536T
  ±7.5mm vertical aperture
    6mm total side gap for SR
  10-3 field accuracy
Similar to CEBAF upgrade

## Slide 32: Tooling Design
Full mould
all pieces and central plug, printed double wall thickness for strength
“Spider”
Channels for half the pieces
Can be flipped over to get other half
Corner holes for ¼”-20 threaded rods throughout, provide loose alignment, constraint

## Slide 33: Can 3D print all parts in place
0.3mm spacing between pieces minimum possible with our printers

## Slide 34: Point field measurement tool for Hall probe, also a “spider”
Single-axis Hall probe inserted in X and Y directions in cross-shaped holes, depth is controlled the centre of magnet length
Used this to confirm field of all 24 wedges at 7 locations  rough magnetisation vector measurement

## Slide 35: Assembly Sandwich

## Slide 36: Assembly Process
1.
2.
3.
4.
5.

## Slide 37: Half Assembled (Metal Frame)
Bought sets of 24 permanent magnet wedges from AllStar Magnetics
Material grade N42EH
Br=1.30T
45mm length

## Slide 38: Assembled Magnet (Plastic+Metal)
Outer ½” thick aluminium frame for strength

## Slide 39: Assembled Magnet
Outer ½” thick aluminium frame for strength

## Slide 40: Endcaps for Safety (no shims here)

## Slide 41: High fields exist in aperture

## Slide 42: Fieldmap Measurement
Used Senis 3MH6 teslameter with 3-axis Hall probe
  Accurate to ±0.01%
Two (horizontal X,Z) linear movement stages
  Accurate to 1um
±10.5mm × 200mm
  0.5mm, 2.5mm steps
8 repeated scans

## Slide 43: Fieldmap Measurement

## Slide 44: Graphical Fieldmap Plot
Left: linear colour scale
Right: log colour map,
field inversion (flux return) far from magnet is visible

## Slide 45: Aperture after Brass Shims (Run 2)

## Slide 46: Magnet with Iron Tuning Rods

## Slide 47: Magnet with Iron Tuning Rods

## Slide 48: Maximum Field Error History
Original
Brass shims
Iter 1, rev. X axis
Iter 1, correct X axis
Iter 1, verify, block slip?
No tuning rods
Iter 1
Iter 2
Iter 3

## Slide 49: Integrated Fields (Run 9)
Chart: 
| 1.2E-2 | 1.15E-2 | 1.0999999999999999E-2 | 1.0500000000000001E-2 | 0.01 | 9.4999999999999998E-3 | 8.9999999999999993E-3 | 8.5000000000000006E-3 | 8.0000000000000002E-3 | 7.4999999999999997E-3 | 7.0000000000000001E-3 | 6.4999999999999997E-3 | 6.0000000000000001E-3 | 5.4999999999999997E-3 | 5.0000000000000001E-3 | 4.4999999999999997E-3 | 4.0000000000000001E-3 | 3.5000000000000001E-3 | 3.0000000000000001E-3 | 2.5000000000000001E-3 | 2E-3 | 1.5E-3 | 1E-3 | 5.0000000000000001E-4 | 1.04083409E-17 | -5.0000000000000001E-4 | -1E-3 | -1.5E-3 | -2E-3 | -2.5000000000000001E-3 | -3.0000000000000001E-3 | -3.5000000000000001E-3 | -4.0000000000000001E-3 | -4.4999999999999997E-3 | -5.0000000000000001E-3 | -5.4999999999999997E-3 | -6.0000000000000001E-3 | -6.4999999999999997E-3 | -7.0000000000000001E-3 | -7.4999999999999997E-3 | -8.0000000000000002E-3 | -8.5000000000000006E-3 | -8.9999999999999993E-3 | -9.4999999999999998E-3 | -0.01 | -1.0500000000000001E-2 | -1.0999999999999999E-2 | -1.15E-2 | -1.2E-2
avg iBx/L (T) | -0.013374 | -0.012294 | -0.011372 | -0.010372 | -0.0094553 | -0.0085976 | -0.0077619 | -0.0068806 | -0.0060013 | -0.0052113 | -0.0044557 | -0.003637 | -0.002821 | -0.0021183 | -0.0013481 | -0.00058805 | 0.00020409 | 0.00093702 | 0.0017421 | 0.0024916 | 0.0032711 | 0.0039927 | 0.0047231 | 0.0054922 | 0.0062953 | 0.0070439 | 0.0077767 | 0.0085771 | 0.0094515 | 0.0103 | 0.011166 | 0.012052 | 0.012933 | 0.013793 | 0.014618 | 0.015505 | 0.016394 | 0.017164 | 0.017949 | 0.018682 | 0.019292 | 0.019754 | 0.020134 | 0.020555 | 0.020874 | 0.021168 | 0.021561 | 0.022101 | 0.022766
avg iBy/L (T) | -0.30835 | -0.33717 | -0.36563 | -0.39365 | -0.42149 | -0.44933 | -0.4772 | -0.50495 | -0.53263 | -0.56042 | -0.58823 | -0.61602 | -0.64372 | -0.67155 | -0.69942 | -0.72721 | -0.75505 | -0.78285 | -0.81074 | -0.83849 | -0.86625 | -0.89408 | -0.92192 | -0.94966 | -0.97743 | -1.0053 | -1.0332 | -1.061 | -1.0887 | -1.1166 | -1.1444 | -1.1722 | -1.1999 | -1.2277 | -1.2553 | -1.283 | -1.3105 | -1.3382 | -1.3659 | -1.3935 | -1.4213 | -1.4493 | -1.4775 | -1.5057 | -1.534 | -1.5621 | -1.59 | -1.617 | -1.6433
avg iBz/L (T) | 0.0058618 | 0.0064108 | 0.0069546 | 0.0074885 | 0.0080165 | 0.0085483 | 0.0090775 | 0.0096132 | 0.01014 | 0.010666 | 0.011208 | 0.011743 | 0.012265 | 0.012801 | 0.013326 | 0.013866 | 0.014391 | 0.014931 | 0.01548 | 0.016003 | 0.016545 | 0.017093 | 0.017627 | 0.018142 | 0.018676 | 0.019207 | 0.019744 | 0.020295 | 0.020821 | 0.021366 | 0.021887 | 0.02243 | 0.022974 | 0.023521 | 0.024041 | 0.024584 | 0.025115 | 0.025679 | 0.026233 | 0.026796 | 0.027409 | 0.027997 | 0.028643 | 0.029265 | 0.029902 | 0.030489 | 0.031108 | 0.031606 | 0.031977
Bx error (T) | -0.0017571 | -0.0014279 | -0.0012573 | -0.0010086 | -0.00084289 | -0.00073638 | -0.00065198 | -0.00052189 | -0.00039377 | -0.00035503 | -0.00035065 | -0.00028318 | -0.00021846 | -0.00026698 | -0.00024798 | -0.00023919 | -0.00019828 | -0.00021658 | -0.00016274 | -0.0001645 | -0.00013615 | -0.0001658 | -0.0001867 | -0.00016881 | -0.00011694 | -0.00011954 | -0.00013795 | -8.882e-05 | 3.4318e-05 | 0.00013152 | 0.00024652 | 0.00038087 | 0.00051083 | 0.00061948 | 0.00069303 | 0.00082923 | 0.00096719 | 0.00098539 | 0.0010196 | 0.0010009 | 0.00086028 | 0.00057072 | 0.00019974 | -0.00013067 | -0.00056298 | -0.0010196 | -0.001378 | -0.0015891 | -0.0016753
By error (T) | 0.0011543 | 0.00015984 | -0.00048753 | -0.00068894 | -0.00071155 | -0.00073974 | -0.00079524 | -0.00072143 | -0.00059132 | -0.0005639 | -0.0005518 | -0.0005307 | -0.00040906 | -0.00042445 | -0.00047562 | -0.00045508 | -0.00047801 | -0.00045468 | -0.00053296 | -0.00046246 | -0.00040502 | -0.00042144 | -0.00044412 | -0.00037452 | -0.00032457 | -0.00037849 | -0.0004542 | -0.0004358 | -0.00035801 | -0.00038995 | -0.00041271 | -0.00039065 | -0.00023339 | -0.00019404 | -6.3521e-05 | 0.00013545 | 0.00039576 | 0.00049923 | 0.00068097 | 0.00084064 | 0.00082549 | 0.00066666 | 0.00027754 | -6.4686e-05 | -0.00052799 | -0.00084064 | -0.00089554 | -0.00015688 | 0.0013563
Good field region ±10.5mm
RHS
RHS

## Slide 50: Integrated Field Error History
Gradual improvement over runs 6-9
Short magnets often require more iterations because of end field effects

## Slide 51: Prototype Magnet Conclusion
A short section of magnet similar to CEBAF upgrade FFA has been tuned to <10-3 accuracy
  No glue/epoxy was used (might reuse wedges), so some issues with blocks staying in place
Temperature variation and material thermal coefficient appears to be the main source of measurement error now
  Working on temperature-controlled enclosure

## Slide 52: Similar Permanent Magnets Built in Industry and Tested with Beam
F
D
1cm grid
These are for a medical proton beamline, hence no open midplane, but higher field (1.85T), similar in width to CEBAF magnet

## Slide 53: Test Beamline Magnet Parameters
Parameter | F magnet | D magnet | Unit
Material | NdFeB |  | 
Grade | N42EH |  | 
Remnant field Br | 1.30 |  | T
Area | 69.90 | 93.88 | cm2
Full aperture | 64.7 × 12 | 48.1 × 12 | mm
Good field region x | ±26.3 | ±18.0 | mm
Maximum field | 1.85 | 1.86 | T

## Slide 54: Nonlinear Magnet Field Profiles
Maximum fields equalised at 1.86T

## Slide 55: Test Beamline Simulated Orbits
10MeV
250MeV
HF
HF
F
F
F
D
D
D
D
10cm grid
Angle 5.625° per cell, 4 cells total = 22.5° (1/8 of an 180° arc)
Half-F magnets on each end  parallel orbits
Cell length 34.4cm, 4 cells total = 1.374m
Lower energy, higher bend angle than CEBAF upgrade

## Slide 56: Magnets Ordered from SABR Enterprises, LLC.

## Slide 57: Orbits within Magnet Models

## Slide 58: Test Beamline with Mounting

## Slide 59: Magnet Construction by Vendor
SABR Enterprises, LLC. in Massachusetts

## Slide 60: Beamline Assembly

## Slide 61: Magnet Apertures

## Slide 62: Fieldmap of one magnet

## Slide 63: Measured Integrated Field
Corrected via fit for Hall probe displacements and tilt angles, <1% error

## Slide 64: Experiment at BNL beamlines
NSRL
  Protons 50-250MeV
  1 day 2 hours
Tandem
  Deuterons 12.9-28MeV
  Equivalent to protons 10-50MeV
    Via rigidity but also window/air energy loss calculation
    Tandem proton max energy is 28.75MeV
  1 day

## Slide 65: Camera and Beam Screen Plates
These were attached to both ends of the beamline.
4 cameras and 4 screens in total.

## Slide 66: NSRL All Energies
Beam in
Beam out

## Slide 67: Tandem All Energies
Beam in
Beam out

## Slide 68: All 12 Ellipses
Beam in
Beam out

## Slide 69: Corrected Centroid X Positions
Beam in
Beam out
Location tracks with energy as expected
Alignment was “by hand”: 3-8mm input errors

## Slide 70: Test Beamline Conclusion
Beams at all energies were transmitted through the 4-cell test girder (22.5° or 1/8 arc)
  Protons at NSRL and deuterons at Tandem
10-250MeV is a factor of 5.3× in momentum
  Very large for a non-scaling FFA
  CEBAF only requires a factor of 2×
Beam ought to propagate several cells around a ring at the start of commissioning
  (even without magnet shimming/correction here)

## Slide 71
Still 1.1GeV linacs
6  11 passes each

## Slide 72: Linac-to-FFA Splitters
Many parameters need to be matched:
  Orbit position and angle x, x’
  Dispersion Dx, Dx’
  Optical functions bx, by, ax, ay
  Time of flight Dt
  Energy derivative of time of flight R56
The last two in particular require separated lines to vary path length for each energy

## Slide 73: Splitter Layout
by Ryan Bodenstein
Blue = dipoles Red = quadrupoles Orange = extraction septa

## Slide 74: Linac-to-FFA Splitter at CBETA ERL
This machine only had 4 different energies, 42-150MeV electrons

## Slide 75
Still 1.1GeV linacs
6  11 passes each

## Slide 76: FFA-to-Linac Transitions
To save money, only use a single line here
Step 1: make all orbits coaxial by matching
  Orbit position and angle x, x’
  Dispersion Dx, Dx’
Step 2: match all the optics simultanously
  Optical functions bx, by, ax, ay
Time of flight is dealt with in the splitter at the other end of the arc

## Slide 77: 1. Adiabatically Reduce Bending
This was also done successfully at CBETA for 4 energies

## Slide 78: 2. Six Energy Coaxial Optics Match
Tricky optimisation

## Slide 79: Conclusion / Status
Pre-CDR/‘white paper’ mostly written (65 pp.)
Permanent magnet irradiation studies in progress (see Ryan Bodenstein IPAC’26 paper)
Next steps are completing design of the splitters and transfer lines  end-to-end simulation
22GeV upgrade is quite far in the future as the Ce+BAF positron upgrade will happen first

## Slide 80: BACKUP

## Slide 81: Tripole Magnet

## Slide 82: Assembly Process Notes
Insert one half of the blocks and then flip the spiders over and insert the other half
Make sure each block is pushed all the way in because they can repel longitudinally
  Actually a mixture of attraction and repulsion
The later blocks will be tighter fit but it was OK with the 0.3mm gaps (0.15mm larger mould)
  Small gaps between some magnets were visible after central plug removed (0.1-0.2mm), inserted brass shims

## Slide 83: Run Sequence
Run 1: bare magnet but bad wedge alignment
Run 2: added brass shims between wedges (better alignment)
Run 3: added 26× 35mil Ø iron tuning rods but got X-axis direction definition wrong!
Run 4: tried first tuning iteration again with corrected X axis
Run 5: verify first tuning iteration with different rod holder but field changed
Run 6: investigate bare magnet without tuning rods again, field had changed, wedge alignment worse perhaps
Run 7: tuning rods first iteration based on run 6
Run 8: 2nd tuning iteration from run 6
Run 9: 3rd tuning iteration from run 6