## Slide 1: Permanent Magnet Investigations
Approach | eRHIC (open midplane) | Cb (can be closed) | Tuning method
PM-driven iron poles | Meng | Witte | Partial short-circuit with iron, fewest variables
Halbach derived | Tsoupas | Tsoupas + Brooks | Block XY movement with screws? Wire EDM cutting?
Rotatable cylinders | Brooks | Brooks | Rotation built into concept
Blocks | Tchoubar + Brooks |  | Block movement with screws?
All methods require tuning to compensate for variability of the PM material blocks
Material-wise, blocks are cheapest followed by cylinders, polygons are most expensive
The magnets with iron poles are probably cheapest and easiest provided interference between the doublet can be compensated for and the poles are good enough

## Slide 2: Which Magnets to Prototype?
Probably best to get real fieldmap of one iron and one not-iron doublet because the fringe field behaviours will be very different
  The not-iron magnet will still have to have an iron shell around it
  The fieldmaps can be put into tracking and strengths re-tuned to get the FFAG momentum window where we want it
Looks like cylinders and Holger’s for Cb
  For eRHIC we’re doing Tsoupas’, Meng’s and Oleg’s