## Slide 1: CBETA Magnets 1501-1503
First girder QF1-QF3

## Slide 2: Last Week
Tue: QF1 iter 2 and E4E survey
Wed: QF2 existing shims but wrong goal strength, did one more iteration, was good
Thu: survey QF2, measure QF3 bare
Fri: QF3 two iterations and survey
Mon: John C. out most of today, QF4?
  Received all survey data from Ming Ke, format looks good, haven’t started processing yet

## Slide 3: 1501 / FG QF1 History
Run # | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
2 | ? | Wrong temperature | 3.38 | 0.114 | Iteration 1 but at wrong temp. with 63mil shims
3 | 12.85 | +0.519% | 62.66 | 2.043 | Bare magnet remeasured at 85F
4 | 1.81 | +0.048% | 6.62 | 0.168 | Wire iteration 1
5 | 1.39 | -0.026% | 5.44 | 0.103 | Wire iteration 2 and normal survey
6 | 1.82 | -0.036% | 6.18 | 0.118 | E4E survey
* New definition with retuned position

## Slide 4: QF1 Comments
This one seems OK for now
  Didn’t quite get to 1 Gauss error
Might have to think about why E4E was different to normal orientation
  Did the shim pack get knocked?
  Is there mathematically something subtle I’m not doing right?

## Slide 5: 1502 / FG QF2 History
Run # | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
8 | ? | Wrong goal field | 7.30 | 0.149 | Old iter 1, correct temperature
32 | 19.55 | -0.642% | 7.31 | 0.153 | Remeasured as-is
33 | 1.20 | -0.053% | 7.18 | 0.109 | Wire iteration
34 | 1.06 | -0.047% | 7.22 | 0.110 | Remeasured morning of survey
* New definition with retuned position

## Slide 6: QF2 Comments
One iteration got it pretty good from its old value, which was tuned at 85F but to the wrong/old strength

## Slide 7: 1503 / FG QF3 History
Run # | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes
17 | ? | Wrong goal field | 4.79 | 0.099 | Old wires tuned to wrong goal field
18 | 18.90 | +0.478% | 95.17 | 2.841 | Wires removed, new measurement
19 | 2.58 | +0.052% | 9.27 | 0.277 | Wire iteration 1
20 | 0.94 | -0.006% | 10.26 | 0.226 | Wire iteration 2, surveyed
* New definition with retuned position

## Slide 8: QF3 Comments
Bare magnet had fairly large multipoles so needed two iterations to get below 1 Gauss error
Didn’t quite recover same low multipoles as before but acceptable

## Slide 9: Harmonics QF1, QF2, QF3
-1.53707 | 0
1.55E-60 | 7.23E-63
10000 | 1.23E-12
-0.83581 | -4.7309
-0.01173 | 0.217055
0.844872 | 4.52217
1.362279 | -2.07543
0.373648 | 1.004986
0.022082 | 0.271097
0.348004 | 0.565561
0.010963 | 0.132249
0.097481 | 0.0135
0.062685 | 8.15E-05
-0.14267 | -0.03825
-0.02755 | -0.05619
0.022478 | -0.05562
0.020426 | -0.03413
0.001893 | -0.04767
0.089107 | -0.042
0.013711 | 0.018641
0.04752 | 0.022667
Displaced magnet by DX (m) | 0.000744
DY (m) | -0.0014
Rotated A/C by (rad) | 0.007782
(deg) | 0.44585
-1.53771 | 0
1.45E-61 | 1.35E-60
10000 | 1.22E-12
-6.44526 | -4.01151
-1.2325 | -4.50123
1.465693 | -0.25837
1.75716 | 4.388536
0.275415 | 0.878044
0.33232 | 0.22798
0.077079 | -0.36988
0.007127 | 0.092834
-0.06907 | -0.23576
-0.10652 | -0.10389
-0.16787 | -0.21118
0.006967 | -0.09321
0.044273 | -0.09139
-0.01053 | -0.02233
-0.01571 | -0.04551
0.065331 | -0.07141
0.046065 | -0.00341
-0.01769 | 0.005993
Displaced magnet by DX (m) | 0.000162
DY (m) | -0.00131
Rotated A/C by (rad) | 0.001994
(deg) | 0.114246
-1.5374 | 0
4.56E-61 | 2.50E-61
10000 | 1.22E-12
-0.10322 | 3.07462
-1.32223 | 1.257384
1.499734 | -1.38853
-0.77255 | 3.225032
-0.2467 | -1.08082
0.024299 | 0.603826
-0.10404 | -0.06343
0.018696 | -0.14664
0.010424 | 0.137437
-0.02734 | -0.05755
0.070416 | 0.018421
-0.01773 | 0.025916
0.012125 | 0.019725
-0.03473 | -0.05335
-0.00934 | 0.036208
0.019426 | -0.08339
-0.00054 | 0.046302
0.042261 | -0.01601
Displaced magnet by DX (m) | 0.000229
DY (m) | -0.00142
Rotated A/C by (rad) | 0.007416
(deg) | 0.424881

## Slide 10: All FG Magnets Status
Magnet name | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes | Run #
BD1 (rb) | 4.07 | +0.058% | 23.55 | 0.773 | New iter 1 | 20
BD2 | 2.63 | -0.196% | 19.28 | 0.539 | 105mil wire | 8
BD3 (rb) | 0.98 | +0.030% | 9.05 | 0.265 | New iter 2 | 15
BD4 | 1.03 | +0.045% | 11.62 | 0.167 | New iter 3 | 9
QF1 | 1.82 | -0.036% | 6.18 | 0.118 | New iter 2 | 6
QF2 | 1.06 | -0.047% | 7.22 | 0.110 | New iter 1 | 34
QF3 (ra) | 0.94 | -0.006% | 10.26 | 0.226 | New iter 2 | 20
QF4 (ra) | ? | Wrong temp | 21.25 | 0.273 | Old iter 1 | 3
* New definition with retuned position
(rb) = rebuilt, (ra) = reassembled from halves

## Slide 11: Next Week
Tue: wire iterations on QF4
Wed: QF4 E4E survey
Thu onwards: BDH if available, otherwise further tuning on BD1 and BD2