## Slide 1: CBETA Magnet 1301, Survey etc.
First girder BD1

## Slide 2: Last Weeks
Christmas week: found top and bottom pairs of tuning wires were touching
  Caused high harmonic noise
  Redesigned 105mil shim holder to fix problem
Last week only 1 day of measurement
  Found sometimes the shim holder was rolled in the magnet by 1-2mm
  Now being more careful about checking placement

## Slide 3: BD1 History, some R&D

## Slide 4: BD1 FOMs Evolution

## Slide 5: BD1 Error Fields Run 30, 31, 32
Strength keeps flip-flopping around by ~0.1%
Iteration isn’t improving it any further

## Slide 6: All FG Magnets Status
Magnet name | Max error on midplane* (Gauss) | Quad strength error | Multipole sqrt(sumsq) (units) | CBETA FOM | Notes | Run #
BD1 (rb) | 2.84 | -0.103% | 7.64 | 0.239 | After R&D | 32
BD2 | 2.63 | -0.196% | 19.28 | 0.539 | 105mil wire | 8
BD3 (rb) | 0.98 | +0.030% | 9.05 | 0.265 | New iter 2 | 15
BD4 | 1.03 | +0.045% | 11.62 | 0.167 | New iter 3 | 9
QF1 | 1.82 | -0.036% | 6.18 | 0.118 | New iter 2 | 6
QF2 | 1.06 | -0.047% | 7.22 | 0.110 | New iter 1 | 34
QF3 (ra) | 0.94 | -0.006% | 10.26 | 0.226 | New iter 2 | 20
QF4 (ra) | 1.35 | +0.068% | 6.48 | 0.200 | New iter 1 | 5
BDH** | 0.32 | +0.005% | 5.50 | 0.158 | Iter 3 | 5
* New definition with retuned position ** Upside-down, needs resurvey
(rb) = rebuilt, (ra) = reassembled from halves

## Slide 7: Survey Data and Software
A sample run of survey data in BMAD/L0E frame was sent to Cornell
  Generally happy with the format
  David Burke will check the fiducials look OK on CAD model
Still need a couple more features
  Optimised magnet positioning
  Compensate for Earth’s magnetic field on BNL coil

## Slide 8: Next Week
Tue: BD1 E4E survey if accepted?
Wed: BD2 tuning
Thu: BD2 survey
Fri: BDH remeasure and resurvey, final E4E
  I’ll continue to develop survey software