## Slide 1: CBETA Window-frame Correctors
WF103, WF104 tested

## Slide 2: Results & Conventions
Serial number | WF103 | WF104
Serial number parity | Odd | Even
Coil placement | Top+bottom | Left+right
B-field axis | B_x=horizontal=“skew” | B_y=vertical=“normal”
Beam deflection kick | Y=vertical | X=horizontal
Goes with Halbach type | D-type (BD, QD etc.) | QF
Readback current in test | 2.991553 A | 2.991464 A
Integrated dipole | 3714.668 G.cm | 3732.459 G.cm
Calibration constant | 1241.719 G.cm/A | 1247.703 G.cm/A
Field angle (rel. to bench) | -90.291° | 0.322°

## Slide 3: Harmonics of Correctors
WF103
WF104
R=25mm as usual, largest is normal sextupole
10000 units = the corrector strength <= 0.03T, no more than 10% main strength
0.003715 | 0
10000 | 2.01E-13
4.524902 | -4.58248
36.54534 | -1.10754
-0.16831 | -0.31324
1.54332 | 0.096101
0.028262 | -0.02234
-0.02184 | 0.010799
-0.0363 | -0.00092
0.002594 | -0.00685
0.002755 | -0.02915
0.025338 | -0.01279
-0.01863 | -0.00836
-0.00975 | -0.02673
0.012919 | 0.006358
0.012556 | 0.005714
-0.01077 | -0.02555
-0.00175 | -0.01849
0.031323 | -0.01588
-0.00488 | 0.003032
-0.0331 | -0.09195
0.003732 | 0
10000 | -4.75E-15
0.221735 | 11.48382
37.02187 | -6.92127
3.529681 | -1.45583
2.698534 | -0.85003
-1.33022 | -0.70256
-1.07617 | 0.097969
1.198841 | -0.02359
0.490408 | 0.277116
-1.03745 | 0.171805
0.958003 | 0.788393
0.78428 | -0.38737
-0.76361 | 0.441551
0.405113 | -0.28789
0.058954 | 0.414142
0.080031 | -0.40976
-1.0923 | -0.70303
2.312357 | -0.04265
-2.97998 | -2.10426
2.367712 | -0.49179

## Slide 4: Status
These correctors are good
Trying to finish calibration of 2nd coil bench
  Measure an electromagnet on both benches
    Determine any calibration difference in electronics
  Measure a Halbach magnet on both benches
    Also includes differences in chiller temperature state
  Derive calibration constant to use in future
    Make 2nd coil replicate 1st coil’s strength
    Multipoles already tested and were same on both coils