## Slide 1: CBETA FFA Response Matrix
And some vague ideas about commissioning

## Slide 2: Full Response Matrices from CBETA-V
FFA correctors  FFA BPMs
One baseline setting and then one-sided differences (1+107=108 settings total)
Horizontal correctors
Vertical correctors

## Slide 3: Get the 107x107 real matrices?
Scott says this takes too long
I say it’s OK if we use the crappy one-sided difference
  108 sets of corrector settings ~15 mins
Why do I want to do this? (once)
  This will show any swapped, disconnected or backwards BPMs as “wrong-looking” rows
  Any swapped, disconnected or backwards correctors as “wrong-looking” columns

## Slide 4: Compare to Real Data (escan.mat)
Below: CBETA-V goes in and out of phase with reality so no wonder we can’t correct globally

## Slide 5: FFA Correction should use Empirical Phase Advances
Many things can make real FFA phase advances be different than CBETA-V
  Hard edge vs. fieldmap vs. actual magnet
  Absolute calibration of magnet strength might be up to ~1% off
  Temperature changes will change quad strength too
The phase advances are the sum over 100+ cells, so they build up over distance
  Not a good idea to use “dead reckoning” from a model that has some errors
Instead, measure phase advances from the machine
  Do this for each energy in a multi-pass configuration
But don’t want to measure 107x107 matrices!
  Solution: make semi-empirical matrix from just 2 kicks

## Slide 6: Calculating Phase Advances from Two Bumps
Energy scan had nice 90deg phase difference, I didn’t bother and just used 2 FFA correctors
  As it happens, this can be fixed afterwards

## Slide 7: Going to Normalised Space
This code makes an oval into not an oval
a[ofs][] and a[ofs+1][] hold the two bumps

## Slide 8: They are both round now I guess
Can get phase advances just by measuring angles from one point to the next

## Slide 9: Phase Advance per Cell
Bad BPMs maybe
I used FFA correctors 1 and 2, so cell 1 is wrong

## Slide 10: Cumulative Phase Advances
(RHS)
I replaced obviously bad data points by the average of their neighbours

## Slide 11: Semi-Empirical Response Matrix
Take the oval shape from the CBETA-V response matrix
Take the phase advances from the real data
Matrix[ab] = make_oval(sin(q),-cos(q))
  where q = phase[b] - phase[a] + 0.1696 radians
    where 0.1696 radians is a fudge that I fit to get the aa diagonal entries right, in other words the phase advance from the corrector to the same cell BPM
  make_oval is just the inverse of unoval
In this case the escan.mat used bumps made from dipoles in the splitter, whereas we want to get the response to FFA correctors like was done in the virtual machine response matrix

## Slide 15: Commissioning Prerequisites
Hysteresis correction for splitter magnets
  We have lots of splitters to set up, so need saved states to load deterministically
  Either “degaussing” oscillation or (difficult but faster to set) state history model
“Pipe cleaning”
  Run grid scans (grid_a_dude) on each splitter line
    Finds any big nonlinear/stray fields
  Do full FFA response matrix (rough) once
    Finds all swapped, missing or reversed correctors and BPMs (rows and columns of response matrix)

## Slide 16: FFA Correction Method
Measure a baseline orbit and then two bump orbits using first two FFA correctors
Calculate the empirical phase advances
Generate the semi-empirical response matrix
Use that matrix in the SVD algorithm for setting the FFA correctors
Can combine with measured FFA responses to splitter magnets too (extra matrix columns)

## Slide 17: Multi-Turn FFA Correction
Repeat the previous slide each time there is a new turn/new energy
Responses for different energies should be quite orthogonal because tunes are different
Can put all this into one SVD, should work well
Can also use orbit differences x2-x1, x3-x2 etc.
  Removes BPM position errors but not scale errors

## Slide 18: BPM Scale Errors from escan.mat
Here I’ve plotted the normalised amplitude of all the energy scan bump pairs
About 6 BPMs with scale errors are visible (generally different scales in X and Y)