## Slide 1: CEBAF 20GeV FFA Magnets
Recap IPAC’21 50% gradient magnet
Updated for a July 30th lattice

## Slide 2: Parameters from IPAC’21 Paper
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 250.91 | -5 | 4 | -0.574 | 1.685
BD | 0.941 | -233.13 | -5 | 4 | 2.107 | 0.008
Take parameters directly from the paper
Peak fields below

## Slide 3: Other Design Rules
Open midplane full height of 4mm (y=±2mm)
  Same as NSLS-IIU upgrade magnet
    Which is also 250T/m
Beam-centroid-to-magnet clearance of 5mm
  Again, same as NSLSII-U, has R=5mm aperture
Br=1.30T material
  E.g. AllStar N42EH grade
    Intrinsic coercivity Hcj=29.0kOe (without radiation)
      I.e. demagnetises totally at m0H=-2.9T (expect “knee” ~-2.7T)

## Slide 4: What about with 100% gradients?
BF converges but is still rather large
Probably should avoid super-high (>150T/m) gradients unless good reason
  E.g. path length
20cm

## Slide 5: Trimming the BD Aperture Range
50% gradient, 2x beam excursion
With reduced BD aperture range
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 125.46 | -10 | 8 | -0.574 | 1.685
BD | 0.941 | -116.57 | -10 | 8 | 2.107 | 0.008
NB: length and bend angles of elements to be multiplied by sqrt(2)
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 125.46 | -10 | 8 | -0.574 | 1.685
BD | 0.941 | -116.57 | -7 | 6.5 | 1.757 | 0.183
Peak fields better balanced between magnets (also minimises SR)

## Slide 6: Finally!
BF
BD
27.8 units error
24.1 units error
10cm
Small magnets, good field, full 5mm clearance
36.7cm2
40.5cm2

## Slide 7: Peak Fields in Updated Lattices
IPAC’21, 50% gradient, BD trimmed design
July 30th lattices
Option | Max Field (T) | SR Loss (MeV) | Final Energy (MeV)
One FFA | 2.007 | 1211.48 | 23418.52
Two FFAs (4+4) | 1.495 | 964.44 | 23665.56
Two FFAs (5+3) | 1.489 | 935.30 | 23694.70
Magnet | Dipole at x=0 (T) | Gradient (T/m) | Xmin (mm) | Xmax (mm) | B(Xmin) (T) | B(Xmax) (T)
BF | 0.681 | 125.46 | -10 | 8 | -0.574 | 1.685
BD | 0.941 | -116.57 | -7 | 6.5 | 1.757 | 0.183
One FFA but only for ~20GeV – energy range issues
Better

## Slide 8: Max Field on Beams
Benchmark on 4+4 FFA2
because highest field in high-energy FFA

## Slide 9: Magnets for July 30th 4+4 FFA2
Wanted to replace central rectangular pieces with wedges to avoid slipping
  Reduce 32 to 24 pieces per magnet (CBETA=16)
BF
BD
27.1 units error
25.8 units error
27.8cm2
27.4cm2
5cm
~25% less area
CBETA magnets were from 38cm2 to 78cm2

## Slide 10: Try Larger Clearances
NSLS-IIU recently doubled their exit slot height from 4mm to 8mm (y=±4mm)
  Allows vacuum chamber inside magnet
Could try doing the same
  Also double beam-to-magnet clearance from 5mm to 10mm (for 20mm full height central aperture)
Rescale gradients on July 30th lattice to 50% to avoid field overshoot in larger clearance gap

## Slide 11: Magnets: 4+4 FFA2, 50% gradient
September 10, 2021
BD
27.1 units error
105.8cm2
BF
32.5 units error
100.4cm2
Should be very similar, but 2x the size and 4x the area
10cm
CBETA magnets were from 38cm2 to 78cm2

## Slide 12: Questions for CEBAF
What beam-centroid-to-pipe distance is considered practical?
  The 10mm-to-magnet should give 7-8mm to pipe
  5mm-to-magnet gives hardly anything
What height should the synchrotron radiation slot be?
  E.g. 8mm full height minus both sides of chamber
  4mm full height seems to small for chamber?
When known, can optimise lattice gradient

## Slide 13: Demagnetisation in IPAC’21 magnets
BF
BD
Red areas show m0H < -1.5T,
yellow -1.5 < m0H < -1.0T, etc.
Stripes are 0.1T intervals.
Looks like worst reverse flux value is around -2.3T, knee is -2.7T, likely OK without radiation but not much margin.

## Slide 14: Demagnetisation in new magnets
BF
BD
Could make the “high field” wedge at the end out of a different material grade, or SmCo

## Slide 15: 50% gradient / large clearance
BF
BD
Very similar, scaled up 2x